## Slide 1: 6.888: Lecture 2 Data Center Network Architectures
Mohammad Alizadeh
Spring 2016
Slides adapted from presentations by Albert Greenberg and Changhoon Kim (Microsoft)

## Slide 2: Data Center Costs
Amortized Cost* | Component | Sub-Components
~45% | Servers | CPU, memory, disk
~25% | Power infrastructure | UPS, cooling, power distribution
~15% | Power draw | Electrical utility costs
~15% | Network | Switches, links, transit
  *3 yr amortization for servers, 15 yr for infrastructure; 5% cost of money
The Cost of a Cloud: Research Problems in Data Center Networks. Sigcomm CCR 2009. Greenberg, Hamilton, Maltz, Patel.

## Slide 3: Server Costs
Ugly secret: 30% utilization considered “good” in data centers
Uneven application fit
  Each server has CPU, memory, disk: most applications exhaust one resource, stranding the others
Long provisioning timescales
  New servers purchased quarterly at best
Uncertainty in demand
  Demand for a new service can spike quickly
Risk management
  Not having spare servers to meet demand brings failure just when success is at hand
Session state and storage constraints
  If the world were stateless servers, life would be good

## Slide 4: Goal: Agility – Any service, Any Server
Turn the servers into a single large fungible pool
  Dynamically expand and contract service footprint as needed
Benefits
  Increase service developer productivity
  Lower cost
  Achieve high performance and reliability
The 3 motivators of most infrastructure projects
Notes: Increase productivity because services can be deployed much faster

## Slide 5: Achieving Agility
Workload management
  Means for rapidly installing a service’s code on a server
  Virtual machines, disk images, containers
Storage Management
  Means for a server to access persistent data
  Distributed filesystems (e.g., HDFS, blob stores)
Network
  Means for communicating with other servers, regardless of where they are in the data center

## Slide 6: Conventional DC Network
Reference – “Data Center: Load balancing Data Center Services”, Cisco 2004
CR
CR
AR
AR
AR
AR
. . .
S
S
DC-Layer 3
Internet
S
S
A
A
A
…
S
S
A
A
A
…
. . .
DC-Layer 2
Key
CR = Core Router (L3)
AR = Access Router (L3)
S = Ethernet Switch (L2)
A = Rack of app. servers
~ 1,000 servers/pod == IP subnet

## Slide 7: Layer 2 vs. Layer 3
Ethernet switching (layer 2)
  Fixed IP addresses and auto-configuration (plug & play)
  Seamless mobility, migration, and failover
  Broadcast limits scale (ARP)
  Spanning Tree Protocol
IP routing (layer 3)
  Scalability through hierarchical addressing
  Multipath routing through equal-cost multipath
  More complex configuration
  Can’t migrate w/o changing IP address

## Slide 8: Conventional DC Network Problems
CR
CR
AR
AR
AR
AR
S
S
S
S
A
A
A
…
S
S
A
A
A
…
. . .
S
S
S
S
A
A
A
…
S
S
A
A
A
…
~ 5:1
~ 40:1
~ 200:1
Dependence on high-cost proprietary routers
Extremely limited server-to-server capacity

## Slide 9: And More Problems …
CR
CR
AR
AR
AR
AR
S
S
S
S
S
S
S
S
S
S
S
S
IP subnet (VLAN) #1
~ 200:1
Resource fragmentation, significantly lowering cloud utilization (and cost-efficiency)
IP subnet (VLAN) #2
A
A
A
…
A
A
A
…
A
A
…
A
A
…
A
A
A

## Slide 10: And More Problems …
CR
CR
AR
AR
AR
AR
S
S
S
S
S
S
S
S
S
S
S
S
IP subnet (VLAN) #1
~ 200:1
Resource fragmentation, significantly lowering cloud utilization (and cost-efficiency)
Complicated manual L2/L3 re-configuration
IP subnet (VLAN) #2
A
A
A
…
A
A
A
…
A
A
…
A
A
…
A
A
A

## Slide 11: Measurements

## Slide 12: DC Traffic Characteristics
Instrumented a large cluster used for data mining and identified distinctive traffic patterns
Traffic patterns are highly volatile
  A large number of distinctive patterns even in a day
Traffic patterns are unpredictable
  Correlation between patterns very weak
Traffic-aware optimization needs to be done frequently and rapidly

## Slide 13: DC Opportunities
DC controller knows everything about hosts
Host OS’s are easily customizable
Probabilistic flow distribution would work well enough, because …
  Flows are numerous and not huge – no elephants
  Commodity switch-to-switch links are substantially thicker (~ 10x) than the maximum thickness of a flow
DC network can be made simple
?
?

## Slide 14: Intuition
Higher speed links improve flow-level load balancing (ECMP)
20×10Gbps
Uplinks
2×100Gbps
Uplinks
11×10Gbps flows
(55% load)
1
2
1
2
20
Prob of 100% throughput = 3.27%
Prob of 100% throughput = 99.95%

## Slide 15: What You Said
“In 3.2, the paper states that randomizing large flows won't cause much perpetual congestion if misplaced since large flows are only 100 MB and thus take 1 second to transmit on a 1 Gbps link. Isn't 1 second sufficiently high to harm the isolation that VL2 tries to provide?”

## Slide 16: Virtual Layer 2 Switch

## Slide 17: VL2 Goals
The Illusion of a Huge L2 Switch
1. L2 semantics
2. Uniform high capacity
3. Performance isolation
A
A
A
…
A
A
A
…
A
A
A
…
A
A
A
…
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A

## Slide 18: VL2 Design Principles
Randomizing to Cope with Volatility
  Tremendous variability in traffic matrices
Separating Names from Locations
  Any server, any service
Embracing End Systems
  Leverage the programmability & resources of servers
  Avoid changes to switches
Building on Proven Networking Technology
  Build with parts shipping today
  Leverage low cost, powerful merchant silicon ASICs, though do not rely on any one vendor

## Slide 19: Single-Chip “Merchant Silicon” Switches
Wedge
6 pack
Switch ASIC
Image courtesy of Facebook

## Slide 20: Specific Objectives and Solutions
Solution
Approach
Objective
2. Uniform high capacity between servers
Enforce hose model using existing mechanisms only
Employ flat addressing
1. Layer-2 semantics
3. Performance Isolation
Guarantee bandwidth for hose-model traffic
Flow-based random traffic indirection (Valiant LB)
Name-location separation & resolution service
TCP

## Slide 21: Discussion

## Slide 22: What You Said
“It is interesting that this paper is from 2009. It seems that a large number of the suggestions in this paper are used in practice today.”

## Slide 23: What You Said
“For address resolution, why not have applications use hostnames and use DNS to resolve hostnames to IP addresses (the mapping from hostname to IP could be updated when a service moved)? Is the directory system basically just DNS but with IPs instead of hostnames?”
“it was unclear why the hash of the 5 tuple is required.”

## Slide 24: Addressing and Routing: Name-Location Separation
VL2
payload
ToR3
. . .
. . .
y
x
Servers use flat names
Switches run link-state routing and maintain only switch-level topology
Cope with host churns with very little overhead
y
z
payload
ToR4
z
ToR2
ToR4
ToR1
ToR3
y, z
payload
ToR3
z
. . .
Directory Service
…
x  ToR2
y  ToR3
z  ToR4
…
Lookup &
Response
…
x  ToR2
y  ToR3
z  ToR3
…

## Slide 25: Addressing and Routing: Name-Location Separation
VL2
payload
ToR3
. . .
. . .
y
x
Servers use flat names
Switches run link-state routing and maintain only switch-level topology
Cope with host churns with very little overhead
y
z
payload
ToR4
z
ToR2
ToR4
ToR1
ToR3
y, z
payload
ToR3
z
. . .
Directory Service
…
x  ToR2
y  ToR3
z  ToR4
…
Lookup &
Response
…
x  ToR2
y  ToR3
z  ToR3
…
Allows to use low-cost switches
Protects network and hosts from host-state churn
Obviates host and switch reconfiguration

## Slide 26: Example Topology: Clos Network
VL2
. . .
. . .
TOR
20 Servers
Int
. . .
. . . . . .
Aggr
K aggr switches with D ports
20*(DK/4) Servers
. . .
. . . . . . . .
Offer huge aggr capacity and multi paths at modest cost

## Slide 27: Example Topology: Clos Network
VL2
. . .
. . .
TOR
20 Servers
Int
. . .
. . . . . .
Aggr
K aggr switches with D ports
20*(DK/4) Servers
. . .
. . . . . . . .
Offer huge aggr capacity and multi paths at modest cost
D (# of 10G ports) | Max DC size (# of Servers)
48 | 11,520
96 | 46,080
144 | 103,680

## Slide 28: Traffic Forwarding: Random Indirection
x
y
payload
T3
y
z
payload
T5
z
IANY
IANY
IANY
IANY
Cope with arbitrary TMs with very little overhead
Links used for up paths
Links used for down paths
T1
T2
T3
T4
T5
T6

## Slide 29: Traffic Forwarding: Random Indirection
x
y
payload
T3
y
z
payload
T5
z
IANY
IANY
IANY
IANY
Cope with arbitrary TMs with very little overhead
Links used for up paths
Links used for down paths
T1
T2
T3
T4
T5
T6
[ ECMP + IP Anycast ]
Harness huge bisection bandwidth
Obviate esoteric traffic engineering or optimization
Ensure robustness to failures
Work with switch mechanisms available today

## Slide 30: What you said
“… the heterogeneity of racks and the incremental deployment of new racks may introduce asymmetry to the topology. In this case, more delicate topology design and routing algorithms are needed. ”

## Slide 31: Some other DC network designs…
Fat-tree [SIGCOMM’08]
Jellyfish (random) [NSDI’12]
BCube [SIGCOMM’10]

## Slide 32: Next time: Congestion Control