## Slide 1: 6.888: Lecture 4 Data Center Load Balancing
Mohammad Alizadeh
Spring 2016

## Slide 2: Motivation
Leaf
1000s of server ports
Multi-rooted tree [Fat-tree, Leaf-Spine, …]
Full bisection bandwidth, achieved via multipathing
Spine
Access
Single-rooted tree
High oversubscription
1000s of server ports
Agg
Core
DC networks need large bisection bandwidth for distributed apps (big data, HPC, web services, etc)
Notes: To set the context, the primary motivation for this work is that datacenter networks need to provide large amounts of bisection bandwidth to support distributed applications; if you consider applications like big data analytics, hPC, or web services, they all require significant network IO between components that are spread across 100s or even 1000s of servers.
In response to this, in recent years, the single rooted tree topologies that have been used in enterprise networks for decades are being replaced with multi-rooted topologies. These new topologies, also called fat-tree or Leaf-Spine, are great -- they can scale bandwidth arbitrarily by just adding more paths; for example, adding more spine switches in a Leaf-Spine design.

## Slide 3: Motivation
Leaf
1000s of server ports
Multi-rooted tree [Fat-tree, Leaf-Spine, …]
Full bisection bandwidth, achieved via multipathing
Spine
DC networks need large bisection bandwidth for distributed apps (big data, HPC, web services, etc)
Notes: So the whole industry is moving in this direction -- of using multi-rooted topologies to build networks with full or near-full bisection bandwidth.
This is great… but if we take a step back, it’s not really what we want.

## Slide 4: Multi-rooted != Ideal DC Network
1000s of server ports
Ideal DC network:
Big output-queued switch
No internal bottlenecks  predictable
Simplifies BW management [Bw guarantees, QoS, …]
Multi-rooted tree
1000s of server ports
Can’t build it 
≈
Possible
bottlenecks
Need efficient load balancing
Notes: A multi-rooted topology is not the “ideal” datacenter network.
What is the ideal network? The ideal network would be a big switch – or more precisely a big output-queued switch. That’s a switch that whenever…

## Slide 5: Today: ECMP Load Balancing
Pick among equal-cost paths by a hash of 5-tuple
Randomized load balancing
Preserves packet order
Problems:
Hash collisions
(coarse granularity)
Local & stateless
(bad with asymmetry;
e.g., due to link failures)
H(f) % 3 = 0

## Slide 6: Solution Landscape
Cong. Oblivious
[ECMP, WCMP,
packet-spray, …]
Cong. Aware
[Flare, TeXCP, CONGA,
DeTail, HULA, …]
Centralized
Distributed
[Hedera, Planck, Fastpass, …]
In-Network
Host-Based
Cong. Oblivious
[Presto]
Cong. Aware
[MPTCP, FlowBender…]

## Slide 7: MPTCP
Slides by Damon Wischik (with minor modifications)

## Slide 8
What problem is MPTCP trying to solve?
Multipath ‘pools’ links.
Two separate links
A pool of links
=
TCP controls how a link is shared.
How should a pool be shared?
Notes: In a circuit-switched network, there is a dedicated channel for each flow. It’s rigid and inflexible: when one flow is silent, the other flow can’t fill in. Packet switching gives you much more flexibility (whether you use it for ATM virtual circuits, or for full-blown IP).
Multipath brings flexibility of the same sort. Pic 3 is rigid and inflexible, Pic 4 is flexible.
In the case of packet switching, you need to be careful about how the flows share the link. Pic 1 circuits made it easy – they give strict isolation between flows. But with Pic 2 packet switching, you need a control plane. It could be with ATM and admission control. Or it could be TCP congestion control, which says how end-systems should adapt their rates so that the network shares its capacity fairly.
What sort of control plane do we need, to ensure that a multipath network works well?

## Slide 9: Application: Multihomed web server
100Mb/s
100Mb/s
2 TCPs @ 50Mb/s
4 TCPs @ 25Mb/s
Notes: Web server, dual-homed. ... This is, ideally, what should happen.

## Slide 10: Application: Multihomed web server
100Mb/s
100Mb/s
2 TCPs @ 33Mb/s
1 MPTCP @ 33Mb/s
4 TCPs @ 25Mb/s

## Slide 11
100Mb/s
100Mb/s
2 TCPs @ 25Mb/s
2 MPTCPs @ 25Mb/s
4 TCPs @ 25Mb/s
The total capacity, 200Mb/s, is shared out evenly between all 8 flows.
Application: Multihomed web server
Notes: At this point, the total access capacity is shared evenly between all the flows.

## Slide 12: Application: Multihomed web server
100Mb/s
100Mb/s
2 TCPs @ 22Mb/s
3 MPTCPs @ 22Mb/s
4 TCPs @ 22Mb/s
The total capacity, 200Mb/s, is shared out evenly between all 9 flows.
It’s as if they were all sharing a single 200Mb/s link. The two links can be said to form a 200Mb/s pool.

## Slide 13
100Mb/s
100Mb/s
2 TCPs @ 20Mb/s
4 MPTCPs @ 20Mb/s
4 TCPs @ 20Mb/s
The total capacity, 200Mb/s, is shared out evenly between all 10 flows.
It’s as if they were all sharing a single 200Mb/s link. The two links can be said to form a 200Mb/s pool.
Application: Multihomed web server

## Slide 14: Application: WIFI & cellular together How should your phone balance its traffic across very different paths?
wifi path: high loss, small RTT
3G path: low loss, high RTT
Notes: It’s obviously good to use both interfaces, to get reliability. But if you just transmit away full blast, is it unfair to the other users?
If you decide not to blast away, how should you balance your traffic, when the paths are so different?

## Slide 15: Application: Datacenters
Can we make the network behave like a large pool of capacity?

## Slide 16
MPTCP is a general-purpose multipath replacement for TCP.

## Slide 17: What is the MPTCP protocol? MPTCP is a replacement for TCP which lets you use multiple paths simultaneously.
TCP
IP
user space
socket API
MPTCP
MPTCP
addr1
addr2
addr
The sender stripes packets across paths
The receiver puts the packets in the correct order
Notes: I’m interested in the congestion control component.
What I talk about is generic: if you want multipath CompoundTCP, or multipath SCTP, or multipath CubicTCP, you’ll need to face the same design issues. We have made our algorithm fit nicely with TCP, but merely as a starting point.

## Slide 18: What is the MPTCP protocol? MPTCP is a replacement for TCP which lets you use multiple paths simultaneously.
TCP
IP
user space
socket API
MPTCP
MPTCP
addr
addr
The sender stripes packets across paths
The receiver puts the packets in the correct order
port p1
port p2
a switch with port-based routing
Notes: I’m interested in the congestion control component.
What I talk about is generic: if you want multipath CompoundTCP, or multipath SCTP, or multipath CubicTCP, you’ll need to face the same design issues. We have made our algorithm fit nicely with TCP, but merely as a starting point.

## Slide 19: Design goal 1: Multipath TCP should be fair to regular TCP at shared bottlenecks
To be fair, Multipath TCP should take as much capacity as TCP at a bottleneck link, no matter how many paths it is using.
Strawman solution: Run “½ TCP” on each path
A multipath TCP flow with two subflows
Regular TCP
Notes: This is the very first thing that comes to mind with multipath TCP, and it’s something that many other people have solved in different ways.
This is just a warm-up... Design Goal 3 is a much “richer” generalization of this goal, which accommodates different topologies, different RTTs. So there’s no point giving an evaluation here.

## Slide 20: Design goal 2: MPTCP should use efficient paths
Each flow has a choice of a 1-hop and a 2-hop path.
How should split its traffic?
12Mb/s
12Mb/s
12Mb/s
Notes: I’m thinking of the paths as given. MPTCP has the choice of how to split its traffic over those given paths.

## Slide 21: Design goal 2: MPTCP should use efficient paths
If each flow split its traffic 1:1 ...
8Mb/s
8Mb/s
8Mb/s
12Mb/s
12Mb/s
12Mb/s

## Slide 22: Design goal 2: MPTCP should use efficient paths
If each flow split its traffic 2:1 ...
9Mb/s
9Mb/s
9Mb/s
12Mb/s
12Mb/s
12Mb/s

## Slide 23: Design goal 2: MPTCP should use efficient paths
If each flow split its traffic 4:1 ...
10Mb/s
10Mb/s
10Mb/s
12Mb/s
12Mb/s
12Mb/s

## Slide 24: Design goal 2: MPTCP should use efficient paths
If each flow split its traffic ∞:1 ...
12Mb/s
12Mb/s
12Mb/s
12Mb/s
12Mb/s
12Mb/s

## Slide 25: Design goal 2: MPTCP should use efficient paths
12Mb/s
12Mb/s
12Mb/s
12Mb/s
12Mb/s
12Mb/s
Theoretical solution (Kelly+Voice 2005; Han, Towsley et al. 2006) MPTCP should send all its traffic on its least-congested paths.
Theorem. This will lead to the most efficient allocation possible, given a network topology and a set of available paths.

## Slide 26: Design goal 3: MPTCP should be fair compared to TCP
Design Goal 2 says to send all your traffic on the least congested path, in this case 3G. But this has high RTT, hence it will give low throughput.
c
d
wifi path: high loss, small RTT
3G path: low loss, high RTT
Goal 3a. A Multipath TCP user should get at least as much throughput as a single-path TCP would on the best of the available paths.
Goal 3b. A Multipath TCP flow should take no more capacity on any link than a single-path TCP would.
Notes: Let’s get back to fairness. This is a more systematic and general way to think about fairness, than the simple bottleneck idea I started with.
If we follow Design Goal 2, we’ll push all our traffic onto the low-loss path, i.e. 3G. But 3G has high RTT, which means that a TCP flow would get low throughput. In order to be fair to TCP, we shouldn’t send very much traffic over 3G. But then the user is suffering because of MPTCP, which is no good.
We want the user to have an incentive to use MPTCP, and we want the network to have an incentive to permit MPTCP. Here’s a more precise way to put it.

## Slide 27: Design goals
Goal 1. Be fair to TCP at bottleneck links
Goal 2. Use efficient paths ...
Goal 3. as much as we can, while being fair to TCP
Goal 4. Adapt quickly when congestion changes
Goal 5. Don’t oscillate
How does MPTCP achieve all this?
Read: “Design, implementation, and evaluation of congestion control for multipath TCP, NSDI 2011”
Notes: “Goal 3. Be fair to TCP” means two things:
fair to the user, i.e. user doesn’t suffer by switching from TCP to MPTCP;
fair to the network, i.e. network doesn’t suffer when users switch from TCP to MPTCP.
It subsumes Goal 1.
There are two more goals.
Paper discusses Goal 4 at length.
Goal 5: we didn’t see any oscillations in our evaluation; theory papers predict no oscillation, for an idealized model.

## Slide 28: How does TCP congestion control work?
Maintain a congestion window w.
Increase w for each ACK, by 1/w
Decrease w for each drop, by w/2

## Slide 29: How does MPTCP congestion control work?
Maintain a congestion window wr, one window for each path, where r ∊ R ranges over the set of available paths.
Increase wr for each ACK on path r, by
Decrease wr for each drop on path r, by wr /2
Notes: MPTCP works pretty much like TCP, i.e. window increases and window decreases on each path. The decrease is the same as TCP. When there is only one path available, this formula reduces to the TCP formula.
We derived a throughput formula for this congestion control algorithm, and checked that it satisfies the design goals.

## Slide 30: Discussion

## Slide 31: What You Said
Ravi: “An interesting point in the MPTCP paper is that they target a 'sweet spot' where there is a fair amount of traffic but the core is neither overloaded nor underloaded.”

## Slide 32: What You Said
Hongzi: “The paper talked a bit of `probing’ to see if a link has high load and pick some other links, and there are some specific ways of assigning randomized assignment of subflows on links. I was wondering does the `power of 2 choices’ have some roles to play here?”

## Slide 33: MPTCP discovers available capacity, and it doesn’t need much path choice.
If each node-pair balances its traffic over 8 paths, chosen at random, then utilization is around 90% of optimal.
FatTree, 128 nodes
FatTree, 8192 nodes
Throughput (% of optimal)
Num. paths
Simulations of FatTree, 100Mb/s links, permutation traffic matrix, one flow per host, TCP+ECMP versus MPTCP.

## Slide 34: MPTCP discovers available capacity, and it shares it out more fairly than TCP+ECMP.
FatTree, 128 nodes
FatTree, 8192 nodes
Throughput (% of optimal)
Flow rank
Simulations of FatTree, 100Mb/s links, permutation traffic matrix, one flow per host, TCP+ECMP versus MPTCP.

## Slide 35: MPTCP can make good path choices, as good as a very fast centralized scheduler.
Simulation of FatTree with 128 hosts.
Permutation traffic matrix
Closed-loop flow arrivals (one flow finishes, another starts)
Flow size distributions from VL2 dataset
Throughput [% of optimal]
Hedera first-fit heuristic
MPTCP

## Slide 36: MPTCP permits flexible topologies
Because an MPTCP flow shifts its traffic onto its least congested paths, congestion hotspots are made to “diffuse” throughout the network. Non-adaptive congestion control, on the other hand, does not cope well with non-homogenous topologies.
Average throughput [% of optimal]
Rank of flow
Simulation of 128-node FatTree, when one of the 1Gb/s core links is cut to 100Mb/s
Notes: This is a very plausible sort of failure!

## Slide 37: MPTCP permits flexible topologies
At low loads, there are few collisions, and NICs are saturated, so TCP ≈ MPTCP
At high loads, the core is severely congested, and TCP can fully exploit all the core links, so TCP ≈ MPTCP
When the core is “right-provisioned”, i.e. just saturated, MPTCP > TCP
Connections per host
Ratio of throughputs, MPTCP/TCP
Simulation of a FatTree-like topology with 512 nodes, but with 4 hosts for every up-link from a top-of-rack switch, i.e. the core is oversubscribed 4:1.
Permutation TM: each host sends to one other, each host receives from one other
Random TM: each host sends to one other, each host may receive from any number

## Slide 38: MPTCP permits flexible topologies
If only 50% of hosts are active, you’d like each host to be able to send at 2Gb/s, faster than one NIC can support.
FatTree
(5 ports per host in total,
1Gb/s bisection bandwidth)
Dual-homed FatTree
(5 ports per host in total,
1Gb/s bisection bandwidth)
1Gb/s
1Gb/s

## Slide 39: Presto
Adapted from slides by Keqiang He (Wisconsin)

## Slide 40: Solution Landscape
Cong. Oblivious
[ECMP, WCMP,
packet-spray, …]
Cong. Aware
[Flare, TeXCP, CONGA,
HULA, DeTail…]
Centralized
Distributed
[Hedera, Planck, Fastpass, …]
In-Network
Host-Based
Cong. Oblivious
[Presto]
Cong. Aware
[MPTCP, FlowBender…]
Is congestion-aware load balancing overkill for datacenters?

## Slide 41: We’ve already seen a congestion-oblivious load balancing scheme
ECMP
Presto is fine-grained congestion-oblivious
load balancing
Key challenge is making this practical

## Slide 42: Key Design Decisions
Use software edge
  No changes to transport (e.g., inside VMs) or switches
LB granularity flowcells [e.g. 64KB of data]
  Works with TSO hardware offload
  No reordering for mice
  Makes dealing with reordering simpler (Why?)
“Fix” reordering at GRO layer
  Avoid high per-packet processing (esp. at 10Gb/s and above)
End-to-end path control

## Slide 43: Presto at a High Level
vSwitch
NIC
NIC
vSwitch
TCP/IP
Spine
Leaf
TCP/IP
Near uniform-sized data units
Notes: Now let’s see how Presto works at high level.
First Presto load balances on near uniform-sized small data units.

## Slide 44: Presto at a High Level
vSwitch
NIC
NIC
vSwitch
TCP/IP
Spine
Leaf
TCP/IP
Proactively distributed evenly over symmetric network by vSwitch sender
Near uniform-sized data units
Notes: These near uniform-sized data units are proactively distributed evenly over the symmetric network by the virtual switches on the hosts.
Please note that today’s data center networks are commonly constructed by symmetric Clos networks.

## Slide 45: Presto at a High Level
vSwitch
NIC
NIC
vSwitch
TCP/IP
Spine
Leaf
TCP/IP
Proactively distributed evenly over symmetric network by vSwitch sender
Near uniform-sized data units
Notes: This slide illustrates how the uniform-sized data units are distributed evenly over the symmetric network.

## Slide 46: Presto at a High Level
vSwitch
NIC
NIC
vSwitch
TCP/IP
Spine
Leaf
TCP/IP
Receiver masks packet reordering due to multipathing below transport layer
Proactively distributed evenly over symmetric network by vSwitch sender
Near uniform-sized data units
Notes: This kind of fine-grained load balancing scheme can cause packet reordering at the receiver side, therefore, at the receiver side,
Presto masks packet reordering due to multipathing below the transport layer.

## Slide 47: Discussion

## Slide 48: What You Said
Arman: “From an (information) theoretic perspective, order should not be such a troubling phenomenon, yet in real networks ordering is so important. How practical are “rateless codes” (network coding, raptor codes, etc.) in alleviating this problem?”
Amy: “The main complexities in the paper stem from the requirement that servers use TSO and GRO to achieve high throughput. It is surprising to me that people still rely so heavily on TSO and GRO. Why doesn't someone build a multi-core TCP stack that can process individual packets at line rate in software?”

## Slide 49: Presto LB Granularity
Presto: load-balance on flowcells
What is flowcell?
  A set of TCP segments with bounded byte count
  Bound is maximal TCP Segmentation Offload (TSO) size
    Maximize the benefit of TSO for high speed
    64KB in implementation
What’s TSO?
TCP/IP
NIC
Segmentation & Checksum Offload
MTU-sized Ethernet Frames
Large Segment
Notes: Instead, Presto load balances on flowcells.
Flowcell essentially is a set of TCP segments with bounded byte count. The bound is the maximal TCP Segmentation Offload (TSO) size
because we want to maximize the benefit of TSO for high speed.
It was 64KB in our implementation.
So, what’s TSO? When a system needs to send large chunks of data, TCP/IP stack operates on large segments and passes
those large segments down to the NIC. Then NIC TSO helps perform segmentation and checksumming.
TSO technique can help reduce processing overhead of the end host stack.

## Slide 50: Presto LB Granularity
Presto: load-balance on flowcells
What is flowcell?
  A set of TCP segments with bounded byte count
  Bound is maximal TCP Segmentation Offload (TSO) size
    Maximize the benefit of TSO for high speed
    64KB in implementation
Examples
25KB
30KB
30KB
Flowcell: 55KB
TCP segments
Start
Notes: To better understand the concept of flowcell, here we show a few examples.
The first example, we show the first three segments of a TCP flow, whose size is 25KB, 30KB and 30KB respectively.
In this case, the first two TCP segments belong to 1 flowcell.

## Slide 51: Intro to GRO
Generic Receive Offload (GRO)
  The reverse process of TSO
Notes: First, we need to introduce a technique called Generic Receiver Offload, or GRO.
GRO is the reverse process of TSO.

## Slide 52: Intro to GRO
TCP/IP
GRO
NIC
OS
Hardware
Notes: GRO logic is located below the TCP/IP stack in the OS and above the NIC.

## Slide 53: Intro to GRO
TCP/IP
GRO
NIC
MTU-sized
Packets
P2
P3
P4
P5
P1
Queue head
Notes: Now let’s see how GRO logic works.
Let’s say a bunch of MTU-sized small packets arrive at the NIC’s queue.

## Slide 54: Intro to GRO
TCP/IP
GRO
NIC
MTU-sized
Packets
P2
P3
P4
P5
P1
Merge
Queue head
Notes: Then GRO logic tries to merge those MTU-sized packet into large TCP segments.

## Slide 55: Intro to GRO
TCP/IP
GRO
NIC
MTU-sized
Packets
P2
P3
P4
P5
P1
Merge
Queue head

## Slide 56: Intro to GRO
TCP/IP
GRO
NIC
MTU-sized
Packets
P3
P4
P5
P1 – P2
Merge
Queue head

## Slide 57: Intro to GRO
TCP/IP
GRO
NIC
MTU-sized
Packets
P4
P5
P1 – P3
Merge
Queue head

## Slide 58: Intro to GRO
TCP/IP
GRO
NIC
MTU-sized
Packets
P5
P1 – P4
Merge
Queue head

## Slide 59: Intro to GRO
TCP/IP
GRO
NIC
MTU-sized
Packets
P1 – P5
Push-up
Large TCP segments are pushed-up at the end of a batched IO event
(i.e., a polling event)
Notes: The merged large TCP segments are pushed-up to TCP/IP at the end of a batched IO event, or a polling event.

## Slide 60: Intro to GRO
TCP/IP
GRO
NIC
MTU-sized
Packets
P1 – P5
Push-up
Merging pkts in GRO creates less segments & avoids using substantially more cycles at TCP/IP and above [Menon, ATC’08]
If GRO is disabled, ~6Gbps with 100% CPU usage of one core
Notes: The basic idea behind is GRO is that spending a few cycles to aggregate packets
within GRO creates less segments for TCP and prevents
having to use substantially more cycles at higher layers in the networking stack.
If GRO is disabled, we can only get ~6Gbps throughput with 100% CPU usage of one core.

## Slide 61: Reordering Challenges
P1
P2
P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC
Out of order packets
Notes: Now we will show “how GRO logic is broken in face of massive packet reordering”.
Here we show an example that packets arrive at the NIC our of order.

## Slide 62: Reordering Challenges
P1
P2
P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC
Notes: GRO still tries to merge packets into segments.
It first process P1.

## Slide 63: Reordering Challenges
P1 – P2
P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC
Notes: P2 is merged with P1.

## Slide 64: Reordering Challenges
P1 – P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC
Notes: P3 is merged into the existing segment too.

## Slide 65: Reordering Challenges
P1 – P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC
GRO is designed to be fast and simple; it pushes-up the existing segment immediately when 1) there is a gap in sequence number, 2) MSS reached or 3) timeout fired
Notes: When GRO processes P6, we meet an issue –
GRO logic is designed to be fast and simple; it pushes-up the existing segment immediately when
1)There is a gap in TCP sequence number, or 2)Maximum Segment Size is reached or 3)timeout is fired.
In this case, there is a TCP sequence number gap between “P1-P3” and “P6”.

## Slide 66: Reordering Challenges
P1 – P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC
Notes: So “P1-P3” is pushed-up immediately and P6 becomes the existing segment.

## Slide 67: Reordering Challenges
P1 – P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC
Notes: When GRO processes P4, it meets similar problem – there is a sequence number gap.
Therefore, P6 is pushed-up and P4 becomes the existing segment.

## Slide 68: Reordering Challenges
P1 – P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC
Notes: This process continues…

## Slide 69: Reordering Challenges
P1 – P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC
Notes: This process continues…

## Slide 70: Reordering Challenges
P1 – P3
P6
P4
P7
P5
P8
P9
TCP/IP
GRO
NIC
Notes: This process continues…

## Slide 71: Reordering Challenges
P1 – P3
P6
P4
P7
P5
P8 – P9
TCP/IP
GRO
NIC
Notes: P9 can be merged with P8.

## Slide 72: Reordering Challenges
P1 – P3
P6
P4
P7
P5
P8 – P9
TCP/IP
GRO
NIC
Notes: Finally, all the packets are pushed-up to TCP/IP.

## Slide 73: Reordering Challenges
GRO is effectively disabled
Lots of small packets are pushed up to TCP/IP
Huge CPU processing overhead
Poor TCP performance due to massive reordering
Notes: We can see that, in case of massive packet oredering, GRO is effectively disabled.
Lots of small packets are pushed-up to TCP/IP.
This has two unfortunate consequences:1) There is huge CPU processing overhead on the end-host because
the networking stack needs to process those small packets 2)TCP performance is poor due to massive packet reordering.

## Slide 74: Handling Asymmetry
40G
40G
40G
40G
40G
40G
Handling asymmetry optimally needs traffic awareness

## Slide 75: Handling Asymmetry
40G
40G
40G
40G
40G
30G
30G
(UDP)
40G
(TCP)
Handling asymmetry optimally needs traffic awareness
35G
5G