## Slide 1: Packet Transport Mechanisms for Data Center Networks
Mohammad Alizadeh
NetSeminar (April 12, 2012)
Stanford University

## Slide 2: Data Centers
Huge investments: R&D, business
  Upwards of $250 Million for a mega DC
Most global IP traffic originates or terminates in DCs
  In 2011 (Cisco Global Cloud Index):
    ~315ExaBytes in WANs
    ~1500ExaBytes in DCs
Notes: Cisco forcasts: in 2011: ~300ExaBytes/year in IP WAN networks, ~1.5ZettaBytes/year in DC (forcasts show similar growth at 32% CAGR until 2015)
Facebook IPO: in 2011 out of $806m total cost of revenue, $606m was spent on DC

## Slide 3
This talk is about packet transport inside the data center.

## Slide 4
INTERNET
Servers
Fabric

## Slide 5
INTERNET
Servers
Fabric
Layer 3
TCP
Layer 3: DCTCP
Layer 2: QCN
Notes: “Specifically, when your computer communicates with a server in some data center, it most-likely uses the TCP for packet transport”
There is also a lot of communication that needs to happen between the servers inside the data center – In fact, more than 75% of all data center traffic stays within the data center. I'm going to be talking about 2 algorithms that have been designed for this purpose: DCTCP & QCN. In the interest of time, I will be focusing mostly on DCTCP, but will discuss some of the main ideas in QCN as well.

## Slide 6: TCP in the Data Center
TCP is widely used in the data center (99.9% of traffic)
But, TCP does not meet demands of applications
  Requires large queues for high throughput:
    Adds significant latency due to queuing delays
    Wastes costly buffers, esp. bad with shallow-buffered switches
Operators work around TCP problems
  Ad-hoc, inefficient, often expensive solutions
  No solid understanding of consequences, tradeoffs
Notes: TCP has been the dominant transport protocol in the Internet for 25 years and is widely used in the data center as well.
However, it was not really designed for this environment and does not meet the demands of data center applications.

## Slide 7: Roadmap: Reducing Queuing Latency
TCP:
~1–10ms
DCTCP & QCN:
~100μs
HULL:
~Zero Latency
Baseline fabric latency (propagation + switching): 10 – 100μs
Notes: "With TCP, queuing delays can be in the milliseconds; more than 3 orders or magnitude larger than the baseline"

## Slide 8: Data Center TCP
with Albert Greenberg, Dave Maltz, Jitu Padhye, Balaji Prabhakar, Sudipta Sengupta, Murari Sridharan
SIGCOMM 2010

## Slide 9: Case Study: Microsoft Bing
A systematic study of transport in Microsoft’s DCs
  Identify impairments
  Identify requirements
Measurements from 6000 server production cluster
More than 150TB of compressed data over a month
Notes: So I would like to next talk a little bit about a measurement study that was done during an internship at Microsoft in 2009. Our goal was to do a systematic...

## Slide 10: Search: A Partition/Aggregate Application
TLA
MLA
MLA
Worker Nodes
………
Picasso
“Everything you can imagine is real.”
“Bad artists copy.
Good artists steal.”
“It is your work in life that is the ultimate seduction.“
“The chief enemy of creativity is good sense.“
“Inspiration does exist,
but it must find you working.”
“I'd like to live as a poor man
with lots of money.“
“Art is a lie that makes us
realize the truth.
“Computers are useless.
They can only give you answers.”
1.
2.
3.
…..
1. Art is a lie…
2. The chief…
3.
…..
1.
2. Art is a lie…
3.
…..
Art is…
Picasso
Strict deadlines (SLAs)
Missed deadline
  Lower quality result
Deadline = 250ms
Deadline = 50ms
Deadline = 10ms
Notes: After the animation, say “this follows what we call the partition/aggregate application structure.
I’ve described this in the context of search, but it’s actually quite general
- “the foundation of many large-scale web applications.”

## Slide 11: Incast
TCP timeout
Worker 1
Worker 2
Worker 3
Worker 4
Aggregator
RTOmin = 300 ms
Synchronized fan-in congestion:
  Caused by Partition/Aggregate.
Vasudevan et al. (SIGCOMM’09)
Notes: Also, this kind of application generates traffic patterns that are particularly problematic for TCP.

## Slide 12: Incast in Bing
Requests are jittered over 10ms window.
Jittering switched off around 8:30 am.
Jittering trades off median against high percentiles.
MLA Query Completion Time (ms)
Notes: 1. Incast really happens – see this actual screenshot from production tool
2. People care, they’ve solved it at application by jittering.
3. They care about the 99.9th percentile, 1-1000 customers

## Slide 13: Data Center Workloads & Requirements
Partition/Aggregate
(Query)
Short messages [50KB-1MB]
(Coordination, Control state)
Large flows [1MB-100MB]
(Data update)
High Burst-Tolerance
Low Latency
High Throughput
The challenge is to achieve these three together.

## Slide 14: Tension Between Requirements
High Burst Tolerance
High Throughput
Low Latency
Deep Buffers:
Queuing Delays
Increase Latency
Shallow Buffers:
Bad for Bursts &
Throughput
We need:
Low Queue Occupancy & High Throughput
Notes: Deep Buffers – bad for latency
Shallow Buffers – bad for bursts & throughput
Reduce RTOmin – no good for latency
AQM – Difficult to tune, not fast enough for incast-style micro-bursts, lose throughput in low stat-mux

## Slide 15: TCP Buffer Requirement
Bandwidth-delay product rule of thumb:
  A single flow needs C×RTT buffers for 100% Throughput.
Throughput
Buffer Size
100%
B
B ≥ C×RTT
B
100%
B < C×RTT
Notes: Now in the case of TCP, the question of how much buffering is needed for high throughput has been studied and is known in the literature as the buffer sizing problem.
End with: “So we need to find a way to reduce the buffering requirements.”

## Slide 16: Reducing Buffer Requirements
Window Size
(Rate)
Buffer Size
Throughput
100%
Appenzeller et al. (SIGCOMM ‘04):
  Large # of flows: is enough.
Notes: Now, there are previous results that show in some circumstances, we don't need big buffers.

## Slide 17: Reducing Buffer Requirements
Appenzeller et al. (SIGCOMM ‘04):
  Large # of flows: is enough
Can’t rely on stat-mux benefit in the DC.
  Measurements show typically only 1-2 large flows at each server
Key Observation:
  Low Variance in Sending Rates  Small Buffers Suffice.
Both QCN & DCTCP reduce variance in sending rates.
  QCN: Explicit multi-bit feedback and “averaging”
  DCTCP: Implicit multi-bit feedback from ECN marks

## Slide 18: DCTCP: Main Idea
How can we extract multi-bit feedback from single-bit stream of ECN marks?
  Reduce window size based on fraction of marked packets.
ECN Marks | TCP | DCTCP
1 0 1 1 1 1 0 1 1 1 | Cut window by 50% | Cut window by 40%
0 0 0 0 0 0 0 0 0 1 | Cut window by 50% | Cut window by 5%
Notes: Start with: “How can we extract multi-bit information from single-bit stream of ECN marks?”
- Standard deviation: TCP (33.6KB), DCTCP (11.5KB)

## Slide 19: DCTCP: Algorithm
Switch side:
  Mark packets when Queue Length > K.
  Sender side:
  Maintain running average of fraction of packets marked (α).
Adaptive window decreases:
  Note: decrease factor between 1 and 2.
B
K
Mark
Don’t
Mark
Notes: very simple marking mechanism
not all the tunings other aqms have
on the source side, the source is tryign to estimate the fraction of packets getting marked
using the obs that there is a stream of ecn marks coming back – more info in the stream than in any single bit
trying to maintain smooth rate variations to operate well even when using shallow buffers, and only a few flows (no stat mux)
F over the last RTT. In TCP there is always a way to get the next RTT from the window size. Comes from the self-clocking of TCP.
Only changing the decrease. Simplest version – makes a lot of sense. So generic could apply it to any algorithm – CTCP, CUBIC – how to cut its window leaving increase part to what it already does. Have to be careful here.

## Slide 20: DCTCP vs TCP
Setup: Win 7, Broadcom 1Gbps Switch
Scenario: 2 long-lived flows,
(Kbytes)
ECN Marking Thresh = 30KB
Notes: Not ns2.

## Slide 21: Evaluation
Implemented in Windows stack.
Real hardware, 1Gbps and 10Gbps experiments
  90 server testbed
  Broadcom Triumph 48 1G ports – 4MB shared memory
  Cisco Cat4948 48 1G ports – 16MB shared memory
  Broadcom Scorpion 24 10G ports – 4MB shared memory
Numerous micro-benchmarks
  – Throughput and Queue Length
  – Multi-hop
  – Queue Buildup
  – Buffer Pressure
Bing cluster benchmark
– Fairness and Convergence
– Incast
– Static vs Dynamic Buffer Mgmt

## Slide 22: Bing Benchmark
Query Traffic
(Bursty)
Short messages
(Delay-sensitive)
Completion Time (ms)
incast
Deep buffers fixes incast, but makes latency worse
DCTCP good for both incast & latency

## Slide 23: Analysis of DCTCP
with Adel Javanmrd, Balaji Prabhakar
SIGMETRICS 2011

## Slide 24: DCTCP Fluid Model
×
N/RTT(t)
W(t)
p(t)
Delay
p(t – R*)
C
+
−
1
0
K
q(t)
Switch
LPF
AIMD
α(t)
Source

## Slide 25: Fluid Model vs ns2 simulations
Parameters: N = {2, 10, 100}, C = 10Gbps, d = 100μs, K = 65 pkts, g = 1/16.
N = 2
N = 10
N = 100

## Slide 26: Normalization of Fluid Model
We make the following change of variables:
The normalized system:
The normalized system depends on only two parameters:

## Slide 27
System has a periodic limit cycle solution.
Example:
Equilibrium Behavior:
Limit Cycles

## Slide 28
System has a periodic limit cycle solution.
Example:
Equilibrium Behavior:
Limit Cycles

## Slide 29: Stability of Limit Cycles
Let X* = set of points on the limit cycle. Define:
A limit cycle is locally asymptotically stable if δ > 0 exists s.t.:

## Slide 30: Poincaré Map
x1
x2
x2 = P(x1)
Stability of Poincaré Map ↔ Stability of limit cycle
x*α = P(x*α)

## Slide 31: Stability Criterion
Theorem: The limit cycle of the DCTCP system:
is locally asymptotically stable if and only if ρ(Z1Z2) < 1.
JF is the Jacobian matrix with respect to x.
T = (1 + hα)+(1 + hβ) is the period of the limit cycle.
Proof: Show that P(x*α + δ) = x*α + Z1Z2δ + O(|δ|2).
We have numerically checked this condition for:

## Slide 32: Parameter Guidelines
How big does the marking
threshold K need to be to
avoid queue underflow?
B
K
Notes: Without getting into details, one can also derive a range for the parameters based on stability and convergence rate considerations.

## Slide 33: HULL: Ultra Low Latency
with Abdul Kabbani, Tom Edsall, Balaji Prabhakar, Amin Vahdat, Masato Yasuda
To appear in NSDI 2012

## Slide 34: What do we want?
TCP:
~1–10ms
DCTCP:
~100μs
~Zero Latency
How do we get this?
C
Incoming Traffic
TCP
Incoming Traffic
DCTCP
K
C

## Slide 35: Phantom Queue
Link
Speed C
Switch
Bump on Wire
Key idea:
  Associate congestion with link utilization, not buffer occupancy
  Virtual Queue (Gibbens & Kelly 1999, Kunniyur & Srikant 2001)
Marking Thresh.
γC
γ < 1 creates
“bandwidth headroom”

## Slide 36: Throughput & Latency vs. PQ Drain Rate
Throughput
Switch latency (mean)

## Slide 37: The Need for Pacing
TCP traffic is very bursty
  Made worse by CPU-offload optimizations like Large Send Offload and Interrupt Coalescing
  Causes spikes in queuing, increasing latency
Example. 1Gbps flow on 10G NIC
65KB bursts every 0.5ms

## Slide 38
Throughput
Switch latency (mean)
Throughput & Latency vs. PQ Drain Rate
(with Pacing)

## Slide 39: The HULL Architecture
Phantom Queue
Hardware
Pacer
DCTCP Congestion Control

## Slide 40: More Details…
Application
DCTCP CC
NIC
Pacer
LSO
Host
Switch
Empty Queue
PQ
Large Flows
Small Flows
Link (with speed C)
ECN Thresh.
γ x C
Large
Burst
Hardware pacing is after segmentation in NIC.
Mice flows skip the pacer; are not delayed.

## Slide 41: Dynamic Flow Experiment 20% load
Load: 20% | Switch Latency (μs) |  | 10MB FCT (ms) | 
 | Avg | 99th | Avg | 99th
TCP | 111.5 | 1,224.8 | 110.2 | 349.6
DCTCP-30K | 38.4 | 295.2 | 106.8 | 301.7
DCTCP-PQ950-Pacer | 2.8 | 18.6 | 125.4 | 359.9
9 senders  1 receiver (80% 1KB flows, 20% 10MB flows).
~93% decrease
~17% increase

## Slide 42: Slowdown due to bandwidth headroom
Processor sharing model for elephants
  On a link of capacity 1, a flow of size x takes
  on average to complete (ρ is the total load).
Example: (ρ = 40%)
1
0.8
Slowdown = 50%
Not 20%

## Slide 43: Slowdown: Theory vs Experiment
Chart: Traffic Load (% of Link Capacity)
| 0.2 | 0.4 | 0.6 | 0.2 | 0.4 | 0.6 | 0.2 | 0.4 | 0.6
Theory | 0.53846 | 0.875 | 2.3333 | 0.29032 | 0.42857 | 0.81818 | 0.19 | 0.28 | 0.48
Experiment | 0.55617 | 0.89642 | 1.6445 | 0.30633 | 0.49331 | 0.82408 | 0.17295 | 0.32119 | 0.5568
DCTCP-PQ800
DCTCP-PQ900
DCTCP-PQ950

## Slide 44: Summary
QCN
  IEEE802.1Qau standard for congestion control in Ethernet
DCTCP
  Will ship with Windows 8 Server
HULL
  Combines DCTCP, Phantom queues, and hardware pacing to achieve ultra-low latency

## Slide 45: Thank you!