## Slide 1
Balaji Prabhakar
Mohammad Alizadeh, Abdul Kabbani, and Berk Atikoglu
Stanford University
Stability Analysis of QCN:
The Averaging Principle

## Slide 2: Outline
Quantized Congestion Notification
  L2 congestion control developed for IEEE802.11Qau
  Fluid model
  Linear control analysis
The Averaging Principle
  A method for improving robustness of control loops to lag
  QCN benefits from the AP

## Slide 3: Background: Layer 2 Congestion Control
Ethernet is the dominant Layer 2 network technology
The 802.1Qbb standard allows per-priority PAUSE
  No packet drops
  Congestion spreading can occur
The 802.1Qau standard allows Ethernet switches to directly signal congestion to Ethernet sources (NICs)
  We’ve been involved in developing QCN (Quantized Congestion Notification) for the IEEE 802.1Qau standard

## Slide 4: Congestion control in the Internet
At the router: DropTail, RED signal congestion by dropping or marking packets using ECN
At the sender: TCP varies the sending rate
Rich history of algorithm development, control-theoretic analysis and detailed simulation of queue management schemes
  Jacobson, Floyd et al, Kelly et al, Low et al, Srikant et al, Misra et al, Katabi et al …

## Slide 5: Ethernet vs. the Internet
Some significant differences …
  No per-packet ACKs in Ethernet, unlike in the Internet
    Not possible to know round trip time
    So congestion must be signaled to the source by switches
    Algorithm not self-clocked
  Sources do not start transmission gently (like TCP slow-start); they can potentially come on at the full line rate of 10Gbps
  Ethernet switch buffers are much smaller than router buffers (100s of KBs vs 100s of MBs)
  Algorithm should be simple enough to be implemented completely in hardware
  Note: QCN has Internet relatives---BIC-TCP at the source and the REM/PI queue management schemes

## Slide 6: Feedback Stabilization in High BDP Networks
In “high BDP” environments, congestion control loops become oscillatory.
  Need feedback stabilization
Two main flavors of feedback stabilization:
  Determine lags (round trip times), apply the correct “gains”
  (e.g. FAST, XCP, RCP, HS-TCP).
  Include higher order queue derivatives of congestion information
  (e.g. REM/PI, XCP, RCP).
We shall see that BIC-TCP and QCN use a different method which we call the Averaging Principle. First, we describe the QCN algorithm.

## Slide 7
QCN

## Slide 8: The QCN Control Loop
Congestion Point
S N
D 1
D N
S 1
Reaction Points
Feedback

## Slide 9: QCN Congestion Point
Consider the single-source, single-switch loop below
Congestion Point (Switch) Dynamics:
Sample packets, compute feedback (Fb), quantize Fb to 6 bits, and reflect only negative Fb values back to Reaction Point.
Source
Qeq
Fb = −(Q-Qeq + w . dQ/dt )
= −(queue offset + w.rate offset)

## Slide 10: QCN Reaction Point
Time
Rate
Current Rate
Congestion message recd
D
D/2
D/4
D/8
Target Rate
RC
RT
Active Increase
Fast Recovery
RAI

## Slide 11: Fluid Model for QCN
Assume N flows pass through a single queue at a switch.
The State variables are RT(t), RC(t), q(t).

## Slide 12: Accuracy: model vs. simulation

## Slide 13: Linear Control Analysis
Linearization around fixed point:
all constants depend
on C, N, ps, Gd, RAI, w
Characteristic Equation

## Slide 14: QCN Stability Margin (Linear Analysis)
Using the Bodé criterion, we obtain:
The QCN control loop is (locally) stable if:
- ω*, b, β, ϒ are known constants depending on C, N, ps, Gd, RAI, w.

## Slide 15: Summary
The algorithm has been extensively tested in deployment scenarios of interest
  Esp. interoperability with link-level PAUSE and TCP
The linear control theoretic analysis gives stability margins, but doesn’t provide any insight as to why QCN (and BIC-TCP) display strong stability in the face of increasing lags.
While attempting to understand this, we have uncovered a general method for improving the stability of congestion control schemes; we present this next

## Slide 16: The Averaging Principle

## Slide 17: The Averaging Principle (AP)‏
A controller (source) is instructed periodically to adjust the input signal (sending rate) to the plant (switch queue).
AP: controller obeys the feedback, and then voluntarily performs averaging as below
IT = Target Input
IC = Current Input

## Slide 18: A Generic Control Example
  As an example, we consider the plant transfer function:

## Slide 19: Step Response Basic AP, No Delay

## Slide 20: Step Response Basic AP, Delay = 8 seconds

## Slide 21: Step Response Two-step AP, Delay = 14 seconds

## Slide 22: Step Response Two-step AP, Delay = 25 seconds
Two-step AP is even more stable than Basic AP

## Slide 23: Averaging in QCN
QCN ~ BIC-TCP
Time
Rate
Congestion message recd
Time
Rate
Current Rate
Congestion message recd
D
D/2
D/4
D/8
Target Rate
RC
RT
Active Increase
RAI
QCN-AIMD ~ TCP

## Slide 24: Stability: QCN-AIMD vs QCN

## Slide 25: Understanding the AP
As mentioned earlier, the two major flavors of feedback compensation are:
  Determine lags, chose appropriate gains
  Feedback higher derivatives of state
We prove that AP is in a sense equivalent to both of the above.
  Very useful since we don’t need to change network switches
  Also, the AP is really very easy to apply; no lag-dependent optimizations of gain parameters needed

## Slide 26: Equivalence of AP and PD
  Main Result:
  Systems 1 and 2 are algebraically equivalent: given identical input sequences, they produce identical output sequences.
Source
does AP
Regular
source
The AP is equivalent to adding a derivative and reducing the gain.

## Slide 27: AP vs PD No Delay

## Slide 28: AP vs PD Delay = 8 seconds

## Slide 29: Proof of Equivalence
Time
Controller
Output
Fb((n-1)T)
Fb(nT)
(n-1)T
nT
(n+1)T
?
−
+
=

## Slide 30: Summary of AP
The AP is a simple method for making many control loops (not just congestion control loops) more robust to increasing lags
Gives an understanding as to the reason why the BIC-TCP and QCN algorithms have such good delay tolerance: they do averaging repeatedly
The AP gives the stabilizing effect of a PD controller, without requiring an additional derivative to be taken at the switch.