## Slide 1: pFabric: Minimal Near-Optimal Datacenter Transport
Mohammad Alizadeh
Shuang Yang, Milad Sharif, Sachin Katti,
Nick McKeown, Balaji Prabhakar, Scott Shenker
Stanford University U.C. Berkeley/ICSI Insieme Networks

## Slide 2: Transport in Datacenters
1000s of server ports
DC network interconnect for distributed compute workloads
Msg latency is King traditional “fairness” metrics less relevant
web
app
db
map-reduce
HPC
monitoring
cache

## Slide 3: Transport in Datacenters
Goal: Complete flows quickly
Requires scheduling flows such that:
  High throughput for large flows
  Fabric latency (no queuing delays) for small flows
Prior work: use rate control to schedule flows
DCTCP[SIGCOMM’10], HULL[NSDI’11], D2TCP[SIGCOMM’12]
D3[SIGCOMM’11], PDQ[SIGCOMM’12], …
vastly improve performance, but complex

## Slide 4: pFabric in 1 Slide
Packets carry a single priority #
e.g., prio = remaining flow size
pFabric Switches
Very small buffers (20-30KB for 10Gbps fabric)
Send highest priority / drop lowest priority pkts
pFabric Hosts
Send/retransmit aggressively
Minimal rate control: just prevent congestion collapse

## Slide 5: Conceptual model

## Slide 6: DC Fabric: Just a Giant Switch
H1
H2
H3
H4
H5
H6
H7
H8
H9

## Slide 7: DC Fabric: Just a Giant Switch
H1
H2
H3
H4
H5
H6
H7
H8
H9
H1
H2
H3
H4
H5
H6
H7
H8
H9
H1
H2
H3
H4
H5
H6
H7
H8
H9
TX
RX

## Slide 8: DC Fabric: Just a Giant Switch
H1
H2
H3
H4
H5
H6
H7
H8
H9
H1
H2
H3
H4
H5
H6
H7
H8
H9
TX
RX

## Slide 9
H1
H2
H3
H4
H5
H6
H7
H8
H9
H1
H2
H3
H4
H5
H6
H7
H8
H9
Objective?
Minimize avg FCT
DC transport = Flow scheduling on giant switch
ingress & egress
capacity constraints
TX
RX

## Slide 10: “Ideal” Flow Scheduling
Problem is NP-hard  [Bar-Noy et al.]
  Simple greedy algorithm: 2-approximation
1
2
3
1
2
3

## Slide 11: pfabric design

## Slide 12: Key Insight
Decouple flow scheduling from rate control
H1
H2
H3
H4
H5
H6
H7
H8
H9
Switches implement flow
scheduling via local mechanisms
Hosts implement simple rate control to avoid high packet loss

## Slide 13: pFabric Switch
Switch Port
7
1
9
4
3
Priority Scheduling send highest priority packet first
Priority Dropping drop lowest priority packets first
6
3
2
5
small “bag” of packets per-port
prio = remaining flow size
H1
H2
H3
H4
H5
H6
H7
H8
H9

## Slide 14: pFabric Switch Complexity
Buffers are very small (~2×BDP per-port)
  e.g., C=10Gbps, RTT=15µs → Buffer ~ 30KB
  Today’s switch buffers are 10-30x larger
  Priority Scheduling/Dropping
  Worst-case: Minimum size packets (64B)
  51.2ns to find min/max of ~600 numbers
  Binary comparator tree: 10 clock cycles
  Current ASICs: clock ~ 1ns

## Slide 15: pFabric Rate Control
With priority scheduling/dropping, queue buildup doesn’t matter
Greatly simplifies rate control
H1
H2
H3
H4
H5
H6
H7
H8
H9
50% Loss
Only task for RC:
Prevent congestion collapse when elephants collide

## Slide 16: pFabric Rate Control
Minimal version of TCP algorithm
Start at line-rate
  Initial window larger than BDP
No retransmission timeout estimation
  Fixed RTO at small multiple of round-trip time
Reduce window size upon packet drops
  Window increase same as TCP (slow start, congestion avoidance, …)
H1
H2
H3
H4
H5
H6
H7
H8
H9

## Slide 17: Why does this work?
Key invariant for ideal scheduling:
At any instant, have the highest priority packet (according to ideal algorithm) available at the switch.
Priority scheduling
  High priority packets traverse fabric as quickly as possible
What about dropped packets?
  Lowest priority → not needed till all other packets depart
  Buffer > BDP → enough time (> RTT) to retransmit

## Slide 18: Evaluation
40Gbps
Fabric Links
10Gbps
Edge Links
9 Racks
ns2 simulations: 144-port leaf-spine fabric
  RTT = ~14.6µs (10µs at hosts)
  Buffer size = 36KB (~2xBDP), RTO = 45μs (~3xRTT)
Random flow arrivals, realistic distributions
  web search (DCTCP paper), data mining (VL2 paper)

## Slide 19: Overall Average FCT
Chart: Load
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
Ideal | 1.0328 | 1.0629 | 1.1142 | 1.1809 | 1.2614 | 1.3645 | 1.4975 | 1.678
pFabric | 1.0405 | 1.0953 | 1.1671 | 1.2578 | 1.3721 | 1.5188 | 1.7144 | 1.9773
PDQ | 1.2874 | 1.3767 | 1.4898 | 1.6316 | 1.82 | 2.0907 | 2.5363 | 3.2155
DCTCP | 1.2576 | 1.5997 | 2.0717 | 2.6692 | 3.3594 | 4.2057 | 5.3579 | 7.1968
TCP-DropTail | 2.1709 | 3.1101 | 4.1956 | 5.6511 | 7.5465 | 10.2482 | 14.3819 | 20.7525
Recall: “Ideal” is REALLY idealized!
    Centralized with full view of flows
    No rate-control dynamics
    No buffering
    No pkt drops
    No load-balancing inefficiency

## Slide 20: Mice FCT (<100KB)
Average
99th Percentile
Almost no jitter
Chart: Load
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
Ideal | 1.0066 | 1.0018 | 1.0026 | 1.0035 | 1.0051 | 1.0061 | 1.007 | 1.008
pFabric | 1.0192 | 1.0359 | 1.0528 | 1.0707 | 1.0896 | 1.1088 | 1.1279 | 1.1435
PDQ | 1.4575 | 1.5373 | 1.6248 | 1.7207 | 1.8388 | 1.9861 | 2.1827 | 2.3968
DCTCP | 1.2777 | 1.5442 | 1.7916 | 2.0476 | 2.3294 | 2.662 | 3.0631 | 3.596
TCP-DropTail | 2.7128 | 3.8866 | 5.0537 | 6.5398 | 8.4256 | 11.0812 | 15.0502 | 20.3733
Chart: Load
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
Ideal | 1.0767 | 1.0729 | 1.0729 | 1.1217 | 1.2259 | 1.2803 | 1.3166 | 1.3535
pFabric | 1.1129 | 1.158 | 1.2136 | 1.3254 | 1.4536 | 1.5605 | 1.6639 | 1.747
PDQ | 2.1723 | 2.5232 | 2.7099 | 2.863 | 3.1297 | 3.5482 | 4.171 | 5.1192
DCTCP | 3.4906 | 4.1598 | 4.5345 | 4.9287 | 5.2966 | 5.7463 | 6.2991 | 7.2011
TCP-DropTail | 27.5707 | 29.8924 | 33.3187 | 40.4708 | 47.6968 | 55.5775 | 63.664 | 72.5742

## Slide 21: Conclusion
pFabric: simple, yet near-optimal
  Decouples flow scheduling from rate control
A clean-slate approach
  Requires new switches and minor host changes
Incremental deployment with existing switches is promising and ongoing work

## Slide 22: Thank You!