## Slide 1: FarmBeats: An IoT System for Data-Driven Agriculture
Deepak Vasisht, Zerina Kapetanovic, Jong-ho Won, Xinxin Jin,
Ranveer Chandra, Ashish Kapoor, Sudipta N. Sinha, Madhusudhan Sudarshan, Sean Stratman

## Slide 2: Why Agriculture?
Agricultural output needs to double by 2050 to meet the demands
– United Nations1
Chart: Population (Billions)
| 1960.0 | 1975.0 | 1989.0 | 2000.0 | 2013.0 | 2026.0 | 2042.0
Population (Billions) | 3 | 4 | 5 | 6 | 7 | 8 | 9
1: United Nations Second Committee (Economic & Financial), 2009

## Slide 3: Why Agriculture?
Agricultural output needs to double by 2050 to meet the demands
– United Nations1
Chart: Population (Billions)
| 1960.0 | 1975.0 | 1989.0 | 2000.0 | 2013.0 | 2026.0 | 2042.0
Population (Billions) | 3 | 4 | 5 | 6 | 7 | 8 | 9
But…
Water levels are receding
Arable land is shrinking
Environment is being degraded
1: United Nations Second Committee (Economic & Financial), 2009

## Slide 4: Why Agriculture?
Agricultural output needs to double by 2050 to meet the demands
– United Nations
Chart: Population (Billions)
| 1960.0 | 1975.0 | 1989.0 | 2000.0 | 2013.0 | 2026.0 | 2042.0
Population (Billions) | 3 | 4 | 5 | 6 | 7 | 8 | 9
Number of World’s Hungry People

## Slide 5: Solution: Data-Driven Agriculture
Ag researchers have shown that it:
Reduces waste
Increases productivity
Ensures sustainability

## Slide 6: But…
According to USDA, high cost of manual data collection prevents farmers from using data-driven agriculture

## Slide 7: IoT System for Agriculture

## Slide 8: Problem 1: No Internet Connectivity
Most farms don’t have any internet coverage
Even if connectivity exists, weather related outages can disable networks for weeks

## Slide 9: Problem 2: No Power on the Farm
Farms do not have direct power sources
Solar power is highly prone to weather variability

## Slide 10: Problem 3: Limited Resources
Need to work with sparse sensor deployments
  Physical constraints due to farming practices
  Too expensive to deploy and maintain

## Slide 11: Beyond Agriculture
How can one design an IoT system in challenging
resource-constrained environments?
Mining
Oil Fields

## Slide 12: In this talk
FarmBeats: An end-to-end IoT system that enables seamless data collection for agriculture
FarmBeats
Farm Services

## Slide 13: In this talk
FarmBeats: An end-to-end IoT system that enables seamless data collection for agriculture
Solves three key challenges:
  Internet Connectivity
  Power Availability
  Limited Sensor Placement
Deployed in two farms in NY and WA for over six months

## Slide 14: Challenge: Internet Connectivity
(Farmer’s home/office)
Cloud

## Slide 15: Challenge: Internet Connectivity
(Farmer’s home/office)
Cloud
Sensors
Few miles away
Obstructed by crops, canopies, etc

## Slide 16: Idea: Use TV White Spaces
Can provide long-range connectivity
Can travel through crops and canopies, because of low frequencies
Large chunks are available in rural areas=> can support large bandwidth

## Slide 17: Idea: Use TV White Spaces
(Farmer’s home/office)
Base Station
TV White Spaces
Cloud
Few miles
Sensors
Weak Connectivity
Prone to outages
Wi-Fi, BLE

## Slide 18: Idea: Compute Locally and Send Summaries
PC on the farm delivers time-sensitive services locally
Combines all the sensor data into summaries
2-3 orders of magnitude smaller than raw data
Cloud delivers long-term analytics and cross-farm analytics

## Slide 19: FarmBeats Design
Gateway PC
(Farmer’s home/office)
Base Station
TV White Spaces
Cloud
Few miles
Sensors

## Slide 20: In this talk
FarmBeats: An end-to-end IoT system that enables seamless data collection for agriculture
Solves three key challenges:
  Internet Connectivity
  Limited Sensor Placement
  Power Availability
Deployed in two farms in NY and WA for over six months

## Slide 21: Challenge: Limited Resources
Need to work with sparse sensor deployments
  Physical constraints due to farming practices
  Too expensive to deploy and maintain
How do we get coverage with a sparse sensor deployment?

## Slide 22: Idea: Use Drones to Enhance Spatial Coverage
Drones are cheap and automatic
Can cover large areas quickly
Can collect visual data
Combine visual data from the drones with the sensor data from the farm

## Slide 23: Idea: Use Drones to Enhance Spatial Coverage
Sparse Sensor Data
Precision Map
Panoramic Overview
Drone Video

## Slide 24: Formulate as a Learning Problem
Training Data
Panoramic Overview
Prediction

## Slide 25: Model Insights
Spatial Smoothness: Areas close to each other have similar sensor values
Visual Smoothness: Areas that look similar have similar sensor values values

## Slide 26: Model
Features (visual)
Kernel (Model visual similarity)
Output (say, moisture)
Spatial Smoothness
Training Phase: Learn K and W
Test Phase: Generate outputs for unknown areas

## Slide 27: Using Sparse Sensor Data
Sensor Data
Precision Map
Panoramic Overview
Drone Video
100 kB summary
FarmBeats can use drones to expand the sparse sensor data and create summaries for the farm

## Slide 28: In this talk
FarmBeats: An end-to-end IoT system that enables seamless data collection for agriculture
Solves three key challenges:
  Internet Connectivity
  Limited Sensor Placement
  Power Availability
Deployed in two farms in NY and WA for over six months

## Slide 29: Challenge: Power Availability is Variable
Gateway
(Farmer’s home/office)
Farm
TV White Spaces
Cloud
Battery dies due to cloudy/rainy/snowy weather

## Slide 30: Challenge: Power Availability is Variable
Solar powered battery saw up to 30% downtime in cloudy months
Miss important data like flood monitoring
How do we deal with weather-based power variability?

## Slide 31: Idea: Weather is Predictable
Use weather forecasts to predict solar energy output
Ration the load to fit within power budget

## Slide 32: Idea: Weather is Predictable
: Duty Cycle ratio, : On time in each cycle, : Off time
Constraints:
  Power Neutrality:
  Minimum Transfer Time:

## Slide 33: Solution: Weather is predictable
Chart: 
| 0.05 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0 | 1.1 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2.0 | 2.1 | 2.2 | 2.3 | 2.4 | 2.5 | 2.6 | 2.7 | 2.8 | 2.9 | 3.0 | 3.1 | 3.2 | 3.3 | 3.4 | 3.5 | 3.6 | 3.7 | 3.8 | 3.9 | 4.0 | 4.1 | 4.2 | 4.3 | 4.4 | 4.5 | 4.6 | 4.7 | 4.8 | 4.9 | 5.0
Y-Value 1 | 20 | 10 | 5 | 3.3333 | 2.5 | 2 | 1.6667 | 1.4286 | 1.25 | 1.1111 | 1 | 0.90909 | 0.83333 | 0.76923 | 0.71429 | 0.66667 | 0.625 | 0.58824 | 0.55556 | 0.52632 | 0.5 | 0.47619 | 0.45455 | 0.43478 | 0.41667 | 0.4 | 0.38462 | 0.37037 | 0.35714 | 0.34483 | 0.33333 | 0.32258 | 0.3125 | 0.30303 | 0.29412 | 0.28571 | 0.27778 | 0.27027 | 0.26316 | 0.25641 | 0.25 | 0.2439 | 0.2381 | 0.23256 | 0.22727 | 0.22222 | 0.21739 | 0.21277 | 0.20833 | 0.20408 | 0.2
Y-Value 2 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10
  Power Neutrality:
  Minimum Transfer Time:
Optimal for minimum latency
FarmBeats can use weather forecasts to duty cycle the base station, with minimum latency

## Slide 34: In this talk
FarmBeats: An end-to-end IoT system that enables seamless data collection for agriculture
Solves three key challenges:
  Internet Connectivity
  Limited Sensor Placement
  Power Availability
Deployed in two farms in NY and WA for over six months

## Slide 35: Deployment
Six months deployment in two farms: Upstate NY (Essex), WA (Carnation)
The farm sizes were 100 acres and 5 acres respectively
Sensors:
  DJI Drones
  Particle Photons with Moisture, Temperature, pH Sensors
  IP Cameras to capture IR imagery as well as monitoring
Cloud Components: Azure Storage and IoT Suite

## Slide 36: Deployment Statistics
Used 10 sensor types, 3 camera types and 3 drone versions
Deployed >100 sensors and ~10 cameras
Collected >10 million sensor measurements, >0.5 million images, 100 drone surveys
Resilient to week long outage from a thunderstorm

## Slide 37: FarmBeats: Usage
Gateway
(Farmer’s home/office)
Farm
TV White Spaces
Cloud

## Slide 38: Example: Panorama
Water puddle
Cow excreta
Cow Herd
Stray cow

## Slide 39: Precision Map: Panorama Generation

## Slide 40: Precision Map : Moisture

## Slide 41: Precision Map : pH

## Slide 42: Precision Map: Accuracy
Chart: Mean Error
| Temp (F) | pH (0-14) | Moist (0-6)
FarmBeats | 0.61 | 0.22 | 0.42
LeastCount | 1 | 0.2 | 0.5
FarmBeats can accurately expand coverage by orders of magnitude using a sparse sensor deployment

## Slide 43: Weather-Aware Duty Cycling
Chart: Day
| 0.0 | 0.917361111030914 | 0.959027777775191 | 1.00069444440305 | 1.04236111103091 | 1.12569444440305 | 1.16736111103091 | 1.20902777777519 | 1.25069444440305 | 1.29236111103091 | 1.33402777777519 | 1.37569444440305 | 1.41736111103091 | 1.45902777777519 | 1.50069444440305 | 1.54236111103091 | 1.58402777777519 | 1.62569444440305 | 1.66736111103091 | 1.70902777777519 | 1.75069444440305 | 1.79236111103091 | 1.83402777777519 | 1.87569444440305 | 1.91736111103091 | 2.01527777779847 | 2.05694444442634 | 2.0986111110542 | 2.14027777779847 | 2.18194444442634 | 2.2236111110542 | 2.26527777779847 | 2.30694444442634 | 2.3486111110542 | 2.39027777779847 | 2.43194444442634 | 2.4736111110542 | 2.51527777779847 | 2.55763888882939 | 2.59930555557366 | 2.64097222220153 | 2.68263888882939 | 2.72430555557366 | 2.76597222220153 | 2.80763888882939 | 2.84930555557366 | 2.89097222220153 | 2.93263888882939 | 2.97430555557366
Y-Value 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 75 | 90 | 90 | 90 | 90 | 90 | 40 | 1 | 1 | 1 | 1 | 1 | 1 | 75 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 75 | 90 | 90 | 90 | 90
Chart: Day
No Duty Cycling

## Slide 44: Weather-Aware Duty Cycling
Chart: Day
| 0.0 | 0.917361111030914 | 0.959027777775191 | 1.00069444440305 | 1.04236111103091 | 1.12569444440305 | 1.16736111103091 | 1.20902777777519 | 1.25069444440305 | 1.29236111103091 | 1.33402777777519 | 1.37569444440305 | 1.41736111103091 | 1.45902777777519 | 1.50069444440305 | 1.54236111103091 | 1.58402777777519 | 1.62569444440305 | 1.66736111103091 | 1.70902777777519 | 1.75069444440305 | 1.79236111103091 | 1.83402777777519 | 1.87569444440305 | 1.91736111103091 | 2.01527777779847 | 2.05694444442634 | 2.0986111110542 | 2.14027777779847 | 2.18194444442634 | 2.2236111110542 | 2.26527777779847 | 2.30694444442634 | 2.3486111110542 | 2.39027777779847 | 2.43194444442634 | 2.4736111110542 | 2.51527777779847 | 2.55763888882939 | 2.59930555557366 | 2.64097222220153 | 2.68263888882939 | 2.72430555557366 | 2.76597222220153 | 2.80763888882939 | 2.84930555557366 | 2.89097222220153 | 2.93263888882939 | 2.97430555557366
Y-Value 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 75 | 90 | 90 | 90 | 90 | 90 | 40 | 1 | 1 | 1 | 1 | 1 | 1 | 75 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 75 | 90 | 90 | 90 | 90
FarmBeats Duty Cycling
Chart: Day
Reduced downtime from 30% to 0% for month long data (September)

## Slide 45: Related Work
Wireless Sensor Networks: Sensor networks for agriculture (Baggio `05, Sanchez et al `11, Lee et al `10,…), LPWAN technologies (LoRA, SIGFOX, …)
Agriculture: Precision agriculture (Bratney et al `99, Mueller et al `12, Cassman et al `99,..), Nutrient measurement (Kim et al `09, Hanson et al `07)
ICTD: Information access and user interfaces (Zhao et al `10, Doerflinger et al 2012)

## Slide 46: Conclusion
FarmBeats: First end to end IoT system for environments constrained by:
    Limited internet connectivity
    Power Variability
    Sparse Sensor Deployment
Acts as a tool to enhance farm and farmer productivity
Used by farmers for applications beyond precision farming

## Slide 47: Thank you!
Sean Stratman, Dancing Crow Farm, WA
Mark & Kirstin Kimball, Essex Farm, NY