## Slide 1: MicroScope: Enabling Microarchitectural Replay Attacks
Dimitrios Skarlatos, Mengjia Yan, Bhargava Gopireddy, Read Sprabery,
Josep Torrellas, and Christopher W. Fletcher
University of Illinois at Urbana-Champaign

## Slide 2: Overview

## Slide 3: The Era of Side-Channels
L2
L2
Core
L3
I-L1
D-L1
L2
Main Memory
Processor
ROB
Branch
TLB
ALU
FPU
Scheduler
Port 0
Port 1
Port 2
Port 3
LSQ
DRAMA’16
TLBLeed’18
Spectre’18
PortSmash’18
Non-Inclusive LLC’19
TLB Contention’13
SGX Prime+Probe[13]
4K-Alliasing’18
Branch
Predictors’16
Subnormal FPU’15

## Slide 4: How much can leak over side channels?
Attacker:
for ..
t1 = time()
use resource
t2 = time()
Victim:
if (secret)
use resource
else
don’t use resource
Need repeated measurements to be confident  Denoise
However, many applications run only once  Attacker gets 1 measurement
Can attackers really extract secrets?

## Slide 5: Contribution: Microarchitectural Replay Attacks
Attacker leverages speculative execution
  To repeatedly replay a snippet of victim code
  That runs only once
ld addr // “replay handle”
…
Victim:
ld secret // secret the attacker tries to leak
Memory operation that will cause a squash and re-execute
}
Primitive to denoise arbitrary
side channels

## Slide 6: Contribution: Microarchitectural Replay Attacks
Issue Replay Handle
Long Latency Event
Time
ld addr:

## Slide 7: Contribution: Microarchitectural Replay Attacks
Issue Replay Handle
Long Latency Event
Speculative Execution of Secret
ld secret:
Time
ld addr:

## Slide 8: Contribution: Microarchitectural Replay Attacks
Issue Replay Handle
Long Latency Event
Squash
Event
Squash
Clear
State
Speculative Execution of Secret
Time
ld addr:
ld secret:

## Slide 9: Contribution: Microarchitectural Replay Attacks
Issue Replay Handle
Long Latency Event
Squash
Event
Clear
State
Replay!!
Cause Shared Resource Contention & Monitor
Speculative Execution of Secret
Squash
ld addr:
ld secret:

## Slide 10: Background

## Slide 11: Page Tables Background
pmd_t
pte_t
PGD
PUD
PMD
PTE
CR3
47 … 39 | 38 … 30 | 29 … 21 | 20 … 12 | 11 … 0
9-bits | 9-bits | 9-bits | 9-bits | Page Offset
+
+
+
+
Address A
Virtual Address
TLB Entry
pgd_t
pud_t
Page tables stored in memory
On a TLB Miss  “page walk” = memory accesses
  Each step of page walk = cache hit/miss.
  Page walk cache (PWC): hardware cache of translations
If Present bit in pte_t is cleared  Page Fault, invoke OS

## Slide 12: Trusted Computing with SGX
Designed to run sensitive applications in the cloud
Do not trust OS/Hypervisor
OS/Hypervisor cannot introspect/tamper enclave
Unfortunately, OS/Hypervisor still manages demand paging
Hardware
Hypervisor
Operating System
App
App
App
Attack Surface With Enclaves
Attack Surface

## Slide 13: Threat Model

## Slide 14: Threat Model
In SGX the OS is responsible
Demand paging
Attacker (OS) can:
Evict TLB entries
Evict page walk cache entries
Monitor side channels

## Slide 15: MicroScope:
A framework to exploit microarchitectural replay attacks

## Slide 16: Attack Examples
//public address
handle(pub_addr);
...
transmit(secret);
...
Victim Code
for i in ...
handle(pub_addrA);
...
transmit(secret[i]);
...
memOp(pub_addrB);
...
Loop Victim Code:

## Slide 17: Terminology
//public address
handle(pub_addr);
...
transmit(secret);
...
Victim Code
Replay handle:
Load to a public address (known to OS)
Transmitter:
Any instruction(s) whose execution reveals secret through some side channel
Occurs < ROB length from Replay Handle

## Slide 18: Timeline of a MicroScope Attack - Setup
Attack
Setup
Victim
Attacker
Time

## Slide 19: Timeline of a MicroScope Attack - Setup
Attack
Setup
Clear PTE
Present Bit of Replay Handle
Victim
Attacker
Time

## Slide 20: Timeline of a MicroScope Attack - Setup
Attack
Setup
Flush Replay Handle Page Table Entries
Victim
Attacker
Clear PTE
Present Bit of Replay Handle
Time

## Slide 21: Timeline of a MicroScope Attack - Setup
Attack
Setup
Flush Replay Handle
TLB Entry
Victim
Attacker
Flush Replay Handle Page Table Entries
Clear PTE
Present Bit of Replay Handle
Time

## Slide 22: Timeline of a MicroScope Attack
Attacker
Victim
Attack
Setup
Issue Replay Handle
Time
handle(pub_addr):

## Slide 23: Timeline of a MicroScope Attack
Attack
Setup
Issue Replay Handle
L1 TLB
Miss
Victim
Attacker
Time
handle(pub_addr):

## Slide 24: Timeline of a MicroScope Attack
Attack
Setup
Issue Replay Handle
L1 TLB
Miss
Speculative Execution of Transmitter
Victim
Attacker
L2 TLB
Miss
Time
handle(pub_addr):
transmit(secret):

## Slide 25: Timeline of a MicroScope Attack
Attack
Setup
Issue Replay Handle
L1 TLB
Miss
L2 TLB
Miss
PWC
Miss
Speculative Execution of Transmitter
Victim
Attacker
Time
handle(pub_addr):
transmit(secret):

## Slide 26: Timeline of a MicroScope Attack
Attack
Setup
Issue Replay Handle
L1 TLB
Miss
L2 TLB
Miss
PWC
Miss
PGD
Walk
PUD
Walk
PMD
Walk
PTE
Walk
Speculative Execution of Transmitter
Victim
Attacker
Time
handle(pub_addr):
transmit(secret):

## Slide 27: Timeline of a MicroScope Attack
Attack
Setup
Issue Replay Handle
L1 TLB
Miss
L2 TLB
Miss
PWC
Miss
PGD
Walk
PUD
Walk
PMD
Walk
PTE
Walk
Victim
Attacker
Tune speculative execution duration with:
Cache Hit or Miss
Speculative Execution of Transmitter
Time
handle(pub_addr):
transmit(secret):

## Slide 28: Timeline of a MicroScope Attack
Attack
Setup
Issue Replay Handle
L1 TLB
Miss
L2 TLB
Miss
PWC
Miss
PGD
Walk
PUD
Walk
PMD
Walk
PTE
Walk
Speculative Execution of Transmitter
Page
Fault
Victim
Attacker
Time
handle(pub_addr):
transmit(secret):

## Slide 29: Timeline of a MicroScope Attack
Squash
Attack
Setup
Issue Replay Handle
L1 TLB
Miss
L2 TLB
Miss
PWC
Miss
PGD
Walk
PUD
Walk
PMD
Walk
PTE
Walk
Speculative Execution of Transmitter
Page
Fault
Victim
Attacker
Time
handle(pub_addr):
transmit(secret):

## Slide 30: Timeline of a MicroScope Attack
Squash
OS
Invocation
Attack
Setup
Issue Replay Handle
L1 TLB
Miss
L2 TLB
Miss
PWC
Miss
PGD
Walk
PUD
Walk
PMD
Walk
PTE
Walk
Speculative Execution of Transmitter
Time
Page
Fault
Victim
Attacker
handle(pub_addr):
transmit(secret):

## Slide 31: Timeline of a MicroScope Attack
Squash
OS
Invocation
Attack
Setup
Issue Replay Handle
L1 TLB
Miss
L2 TLB
Miss
PWC
Miss
PGD
Walk
PUD
Walk
PMD
Walk
PTE
Walk
Speculative Execution of Transmitter
Page
Fault
Victim
Attacker
Page Fault
Handler
handle(pub_addr):
transmit(secret):

## Slide 32: Timeline of a MicroScope Attack
Squash
OS
Invocation
Attack
Setup
Issue Replay Handle
L1 TLB
Miss
L2 TLB
Miss
PWC
Miss
PGD
Walk
PUD
Walk
PMD
Walk
PTE
Walk
Speculative Execution of Transmitter
Page
Fault
Victim
Attacker
Flush Replay Handle Page Table Entries
handle(pub_addr):
transmit(secret):
Page Fault
Handler

## Slide 33: Timeline of a MicroScope Attack
Squash
OS
Invocation
Attack
Setup
Issue Replay Handle
L1 TLB
Miss
L2 TLB
Miss
PWC
Miss
PGD
Walk
PUD
Walk
PMD
Walk
PTE
Walk
Speculative Execution of Transmitter
Page
Fault
Victim
Attacker
Replay!!
handle(pub_addr):
transmit(secret):

## Slide 34: Timeline of a MicroScope Attack
OS
Invocation
Attack
Setup
Issue Replay Handle
L1 TLB
Miss
L2 TLB
Miss
PWC
Miss
PGD
Walk
PUD
Walk
PMD
Walk
PTE
Walk
Squash
Speculative Execution of Transmitter
Page
Fault
Victim
Attacker
handle(pub_addr):
transmit(secret):

## Slide 35: Timeline of a MicroScope Attack
OS
Invocation
Attack
Setup
Issue Replay Handle
L1 TLB
Miss
L2 TLB
Miss
PWC
Miss
PGD
Walk
PUD
Walk
PMD
Walk
PTE
Walk
Squash
Speculative Execution of Transmitter
Page
Fault
Victim
Attacker
handle(pub_addr):
transmit(secret):

## Slide 36: Timeline of a MicroScope Attack
Victim
Attacker Monitor/Contention thread
Cause Shared Resource Contention & Monitor
Replay!!
Squash
OS
Invocation
Attack
Setup
Issue Replay Handle
L1 TLB
Miss
L2 TLB
Miss
PWC
Miss
PGD
Walk
PUD
Walk
PMD
Walk
PTE
Walk
Speculative Execution of Transmitter
Page
Fault
Attacker
handle(pub_addr):
transmit(secret):

## Slide 37: Loop Example

## Slide 38: Loop Example
for i in ...
handle(pub_addrA);
...
transmit(secret[i]);
...
memOp(pub_addrB);
...
Goal:
  Leak secret in every iteration
Challenge:
  Monitor window of a replay handle < ROB length
Victim:

## Slide 39: Loop Example
for i in ...
handle(pub_addrA);
...
transmit(secret[i]);
...
pivot(pub_addrB);
...
Replay Handle
Pivot Instruction
Transmit Code
Victim:
Instruction used to pivot around transmit instructions

## Slide 40: In a Loop
for i in ...
handle(pub_addrA);
...
transmit(secret[i]);
...
pivot(pub_addrB);
...
handle(pub_addrA);
...
transmit(secret[0]);
...
pivot(pub_addrB);
...
handle(pub_addrA);
...
transmit(secret[1]);
...
pivot(pub_addrB);
Monitor window
Replay Handle
Pivot Instruction
Transmit Code
Static Code
Dynamic code
Iteration i=0
Iteration i=1

## Slide 41: In a Loop
handle(pub_addrA);
...
transmit(secret[0]);
...
pivot(pub_addrB);
...
handle(pub_addrA);
...
transmit(secret[1]);
...
pivot(pub_addrB);
Pivot page fault
Replay Handle
Pivot Instruction
Transmit Code
for i in ...
handle(pub_addrA);
...
transmit(secret[i]);
...
pivot(pub_addrB);
...
Static Code
Dynamic code

## Slide 42: In a Loop
handle(pub_addrA);
...
transmit(secret[0]);
...
pivot(pub_addrB);
...
handle(pub_addrA);
...
transmit(secret[1]);
...
pivot(pub_addrB);
Cause page fault on pivot
Replay Handle
Pivot Instruction
Transmit Code
for i in ...
handle(pub_addrA);
...
transmit(secret[i]);
...
pivot(pub_addrB);
...
Static Code
Dynamic code
Retired instructions

## Slide 43: In a Loop
handle(pub_addrA);
...
transmit(secret[0]);
...
pivot(pub_addrB);
...
handle(pub_addrA);
...
transmit(secret[1]);
...
pivot(pub_addrB);
Cause page fault in
new replay handle
Replay Handle
Pivot Instruction
Transmit Code
Static Code
Dynamic code
for i in ...
handle(pub_addrA);
...
transmit(secret[i]);
...
pivot(pub_addrB);
...
Retired instructions

## Slide 44: In a Loop
Retired Instructions
New Monitor Window
Use this idea to denoise side channels on AES
(see paper)
Replay Handle
Pivot Instruction
Transmit Code
handle(pub_addrA);
...
transmit(secret[0]);
...
pivot(pub_addrB);
...
handle(pub_addrA);
...
transmit(secret[1]);
...
pivot(pub_addrB);
Static Code
Dynamic code
for i in ...
handle(pub_addrA);
...
transmit(secret[i]);
...
pivot(pub_addrB);
...

## Slide 45: Port Contention Attack

## Slide 46: Port Contention Attack with MicroScope
Replay Handle
Transmit Code
handle(pub_addrA);
if (secret)
victim_mul()
else
victim_div()
Victim:
Setup replay attack
…
for …
t1 = time()
attacker_div()
t2 =time()
}
Attacker:
Attacker Code
No Loop!

## Slide 47: Port Contention Attack with MicroScope
Replay Handle
Transmit Code
handle(pub_addrA);
if (secret)
victim_mul()
else
victim_div()
Victim:
Victim
Thread
Decode
INT ALU
FP DIV
Attacker
Thread
Setup replay attack
…
for …
t1 = time()
attacker_div()
t2 =time()
}
Attacker:
Attacker Code

## Slide 48: Port Contention Attack with MicroScope
Replay Handle
Transmit Code
handle(pub_addrA);
if (secret)
victim_mul()
else
victim_div()
Victim:
Victim
Thread
Decode
Attacker
Thread
Attacker Code
Setup replay attack
…
for …
t1 = time()
attacker_div()
t2 =time()
}
Attacker:
Victim
Thread
INT ALU
FP DIV
Attacker
Thread

## Slide 49: Port Contention Attack with MicroScope
Replay Handle
Transmit Code
handle(pub_addrA);
if (secret)
victim_mul()
else
victim_div()
Victim:
Victim
Thread
Decode
Attacker
Thread
Attacker Code
Setup replay attack
…
for …
t1 = time()
attacker_div()
t2 =time()
}
Attacker:
Victim
Thread
INT ALU
FP DIV
Attacker
Thread
FP DIV
10,000  1

## Slide 50: Port Contention Results
Victim and attacker run on adjacent SMT contexts of same core
Attacker performs divisions in a loop and measures time
Victim performs two multiplications without a loop
Victim performs two divisions without a loop

## Slide 51: Generalizing Microarchitectural Replay Attacks

## Slide 52: Microarchitectural Replay Attacks
Changing each can result in different attacks!!
Strategy
Measure
Secret
Attacker
Replay Handle
Window
Victim
Replayed
Code
Trigger
Replay?
Side
Channels?
1
2
3
4
 Page fault-inducing load
 Leaky instruction
 uarch structures
 Page fault until denoise
1
2
3
4
This work:
Replay Handle
Replayed Code
Side Channel
Attacker strategy

## Slide 53: More On the Paper
Other attack examples
MicroScope framework implementation
Attacks on AES
Countermeasures discussion

## Slide 54: Open source!
MicroScope Framework
  Denoise nearly arbitrary microarchitectural side channels using page faults
  Only a single run of the victim
  Demonstrate attacks on notoriously noisy side channels
    Detect the presence or absence of two divide instructions
    Single-step and denoise cache-based attacks on AES
https://github.com/dskarlatos/MicroScope

## Slide 55: Takeaways
Microarchitectural Replay Attacks
 New class of attacks
Opens large new attack surface (noisy side channels)
Implications for integrity, TSX, physical side channels
Exploits core microarchitectural feature
  Dynamic instructions can be replayed through controlled squashes!
We need new security properties to mitigate these attacks!