## Slide 1: Scalable Multi-Access Flash Store for Big Data Analytics
Sang-Woo Jun, Ming Liu
Kermin Fleming*, Arvind
Massachusetts Institute of Technology
*Intel, work while at MIT
This work is funded by Quanta and Samsung.
We also thank Xilinx for their generous hardware donations
Notes: Affiliation, elliott at intel , work while at mit
sponsers

## Slide 2: Big Data Analytics
Analysis of previously unimaginable amount of data provides deep insight
Examples:
  Analyzing twitter information to predict flu outbreaks weeks before the CDC
  Analyzing personal genome to determine predisposition to disease
  Data mining scientific datasets to extract accurate models
Likely to be the biggest economic driver for the IT industry for the next 5 or more years
Notes: Start with examples, description in next slide (size, randomness < db sequential)

## Slide 3: Big Data Analytics
Data so large and complex, that traditional processing methods are no longer effective
  Too large to fit reasonably in fast RAM
  Random access intensive, making prefetching and caching ineffective
Data is often stored in the secondary storage of multiple machines on a cluster
  Storage system and network performance become first-order concerns
Notes: Start with examples, description in next slide (size, randomness < db sequential)

## Slide 4: Designing Systems for Big Data
Due to terrible random read latency of disks, analytic systems were optimized for reducing disk access, or making them sequential
Widespread adoption of flash storage is changing this picture
Chart: Latency of system components (μs)
| Disk | 1Gb Ethernet | DRAM
Latency of system components | 2000 | 120 | 0.3
Chart: Latency of system components (μs)
| Flash | 1Gb Ethernet | DRAM
Latency of system components | 100 | 120 | 0.3
Chart: Latency of system components (μs)
| Flash | 1Gb Ethernet | DRAM
Latency of system components | 100 | 120 | 0.3
Modern systems need to balance all aspects of the system to gain optimal performance
rescaled
Notes: Add “re-scaling” to new chart

## Slide 5: Designing Systems for Big Data
Network Optimizations
  High-performance network links (e.g. Infiniband)
Storage Optimizations
  High-performance storage devices (e.g. FusionIO)
  In-Store computing (e.g. Smart SSD)
  Network-attached storage device (e.g. QuickSAN)
Software Optimizations
  Hardware implementations of network protocols
  Flash-aware distributed file systems (e.g. CORFU)
  FPGA or GPU based accelerators (e.g. Netezza)
Cross-layer optimization is required for optimal performance

## Slide 6: Current Architectural Solution
Previously insignificant inter-component communications become significant
When accessing remote storage:
  Read from flash to RAM
  Transfer from local RAM to remote RAM
  Transfer to accelerator and back
CPU
RAM
FusionIO
Infiniband
FPGA
CPU
RAM
FusionIO
Infiniband
FPGA
Motherboard
Motherboard
Hardware and software latencies are additive
Potential bottleneck at multiple transport locations
Notes: Add request packet from cpu to cpu
Loop animations?

## Slide 7: BlueDBM Architecture Goals
Low-latency high-bandwidth access to scalable distributed storage
Low-latency access to FPGA acceleration
Many interesting problems do not fit in DRAM but can fit in flash
CPU
RAM
Flash
Network
FPGA
Motherboard
CPU
RAM
Flash
Network
FPGA
Motherboard
Notes: Add request packet that goes from cpu to remote fpga
Loop animations!

## Slide 8: BlueDBM System Architecture
FPGA manages flash, network and host link
PCIe
…
Node 20
1TB Flash
Programmable
Controller
(Xilinx VC707)
Host PC
Ethernet
Expected to be constructed by summer, 2014
Node 19
1TB Flash
Programmable
Controller
(Xilinx VC707)
Host PC
Node 0
1TB Flash
Programmable
Controller
(Xilinx VC707)
Host PC
A proof-of-concept prototype is functional!
Controller Network
~8 High-speed (12Gb/s)
serial links (GTX)
Notes: Bandwidth numbers? Topology?

## Slide 9: Inter-Controller Network
BlueDBM provides a dedicated storage network between controllers
  Low-latency high-bandwidth serial links (i.e. GTX)
  Hardware implementation of a simple packet-switched protocol allows flexible topology
  Extremely low protocol overhead (~0.5μs/hop)
Controller Network
~8 High-speed (12Gb/s)
serial links (GTX)
…
1TB Flash
Programmable
Controller
(Xilinx VC707)
1TB Flash
Programmable
Controller
(Xilinx VC707)
1TB Flash
Programmable
Controller
(Xilinx VC707)
Notes: Virtual channel? Virtual network?

## Slide 10: Inter-Controller Network
BlueDBM provides a dedicated storage network between controllers
  Low-latency high-bandwidth serial links (i.e. GTX)
  Hardware implementation of a simple packet-switched protocol allows flexible topology
  Extremely low protocol overhead (~0.5μs/hop)
…
1TB Flash
Programmable
Controller
(Xilinx VC707)
1TB Flash
Programmable
Controller
(Xilinx VC707)
1TB Flash
Programmable
Controller
(Xilinx VC707)
Protocol supports virtual channels to ease development
High-speed (12Gb/s)
serial link (GTX)
Notes: Virtual channel? Virtual network?

## Slide 11: Controller as a Programmable Accelerator
BlueDBM provides a platform for implementing accelerators on the datapath of storage device
  Adds almost no latency by removing the need for additional data transport
  Compression or filtering accelerators can allow more throughput than hostside link (i.e. PCIe) allows
Example: Word counting in a document
  Counting is done inside accelerators, and only the result need to be transported to host

## Slide 12: Two-Part Implementation of Accelerators
Accelerators are implemented both before and after network transport
  Local accelerators parallelize across nodes
  Global accelerators have global view of data
Virtualized interface to storage and network provided in these locations
Host
Global Accelerator
Local Accelerator
Local Accelerator
Flash
Flash
e.g., count words
e.g., aggregate count
Network
e.g., count words

## Slide 13: Prototype System (Proof-of-Concept)
Prototype system built using Xilinx ML605 and a custom-built flash daughterboard
  16GB capacity, 80MB/s bandwidth per node
  Network over GTX high-speed transceivers
Flash board is 5 years old, from an earlier project

## Slide 14: Prototype System (Proof-of-Concept)
Hub nodes
Notes: We needed hub nodes because the ML605 only has one SMA port pinned out
Forced to take a switched fabric topology because ML605 has only one SMA port.

## Slide 15: Prototype Network Performance
Chart: Network Hops
| 0 | 2 | 4 | 6 | 8 | 10
#REF! | 432 | 432 | 432 | 432 | 432

#REF! | 0.04 | 1.68 | 2.32 | 3.31 | 4.36 | 5.48

## Slide 16: Prototype Bandwidth Scaling
Chart: Node Count
| 0 | 2 | 4
Prototype performance | 80 | 160 | 310
Chart: Node Count
| 0 | 2 | 4
Prototype performance | 0.08 | 0.16 | 0.31
rescaled
Chart: Node Count
| 0 | 2 | 4
Prototype performance | 0.08 | 0.16 | 0.31
Projected System performance | 1.6 | 3.2 | 6.4
Maximum PCIe bandwidth
Only reachable
by accelerator
Notes: new graph with expected performance
Animation? Show orig, scale, show compare

## Slide 17: Prototype Latency Scaling
Chart: Network Hops
| 0 | 2 | 3
Flash Chip | 27 | 27 | 27
Controller+Network | 41 | 43 | 45
Software | 4 | 4 | 4

## Slide 18: Benefits of in-path acceleration
Less software overhead
Not bottlenecked by flash-host link
Experimented using hash counting
  In-path: Words are counted on the way out
  Off-path: Data copied back to FPGA for counting
  Software: Counting done in software
We’re actually building both configurations
Chart: Bandwidth (MB/s)
| In-datapath | Off-datapath | Software
Bandwidth (MB/s) | 128 | 53 | 31
Notes: Describe in-path vs out-path
Describe the experiment (route data back to FPGA, pipeline bubbles, pcie bottlenecks)

## Slide 19: Work In Progress
Improved flash controller and File System
  Wear leveling, garbage collection
  Distributed File System as accelerator
Application-specific optimizations
  Optimized data routing/network protocol
  Storage/Link Compression
Database acceleration
  Offload database operations to FPGA
  Accelerated filtering, aggregation and compression could improve performance
Application exploration
  Including medical applications and Hadoop

## Slide 20: Thank you
Takeaway: Analytics systems can be made more efficient by using reconfigurable fabric to manage data routing between system components
FPGA
CPU
+
RAM
Network
Flash
FPGA
CPU
+
RAM
Network
Flash

## Slide 21: FPGA Resource Usage

## Slide 22: New System Improvements
A new, 20-node cluster will exist by summer
  New flash board with 1TB of storage at 1.6GB/s
    Total 20TBs of flash storage
  8 serial links will be pinned out as SATA ports, allowing flexible topology
    12Gb/s per link GTX
  Rack-mounted for ease of handling
  Xilinx VC707 FPGA boards
Rackmount
Node 0
Node 1
Node 2
Node 3
Node 4
Node 5
…

## Slide 23: Example: Data driven Science
Massive amounts of scientific data is being collected
  Instead of building an hypothesis and collecting relevant data, extract models from massive data
University of Washington N-body workshop
  Multiple snapshots of particles in simulated universe
  Interactive analysis provides insights to scientists
  ~100GBs, not very large by today’s standards
“Visualize clusters of particles moving faster than X”
“Visualize particles that were destroyed,
After being hotter than Y”

## Slide 24: Workload Characteristics
Large volume of data to examine
Access pattern is unpredictable
  Often only a random subset of snapshots are accessed
Row
Row
Row
Row
Row
Row
Row
Rows of interest
“Hotter than Y”
Row
Row
Row
Row
Row
Row
Row
Snapshot 1
Snapshot 2
Access at
random intervals
“Destroyed?”
Sequential
scan

## Slide 25: Constraints in System Design
Latency is important in a random-access intensive scenario
Components of a computer system has widely different latency characteristics
Chart: 
| Disk | 1Gb Ethernet | Flash | 10Gb Ethernet | Infiniband | DRAM
Latency of system components | 2000 | 120 | 100 | 50 | 4 | 0.3
Chart: 
| 1Gb Ethernet | Flash | 10Gb Ethernet | Infiniband | DRAM
Latency of system components | 120 | 100 | 50 | 4 | 0.3
“even when DRAM in the cluster is ~40% the size of the entire database, [... we could only process] 900 reads per second, which is much worse than the 30,000”
“Using HBase with ioMemory” -FusionIO

## Slide 26: Constraints in System Design
Latency is important in a random-access intensive scenario
Components of a computer system has widely different latency characteristics
Chart: 
| Disk | 1Gb Ethernet | Flash | 10Gb Ethernet | Infiniband | DRAM
Latency of system components | 2000 | 120 | 100 | 50 | 4 | 0.3
“even when DRAM in the cluster is ~40% the size of the entire database, [... we could only process] 900 reads per second, which is much worse than the 30,000”
“Using HBase with ioMemory” -FusionIO

## Slide 27: Existing Solutions - 1
Baseline: Single PC with DRAM and Disk
Size of dataset exceeds normal DRAM capacity
  Data on disk is accessed randomly
  Disk seek time bottlenecks performance
Solution 1: More DRAM
  Expensive, Limited capacity
Solution 2: Faster storage
  Flash storage provides fast random access
  PCIe flash cards like FusionIO
Solution 3: More machines

## Slide 28: Existing Solutions - 2
Cluster of machines over a network
Network becomes a bottleneck with enough machines
  Network fabric is slow
  Software stack adds overhead
Fitting everything on DRAM is expensive
  Trade-off between network and storage bottleneck
Solution 1: High-performance network such as Infiniband

## Slide 29: Existing Solutions - 3
Cluster of expensive machines
  Lots of DRAM
  FusionIO storage
  Infiniband network
Now computation might become the bottleneck
Solution 1: FPGA-based Application-specific Accelerators

## Slide 30: Previous Work
Software Optimizations
  Hardware implementations of network protocols
  Flash-aware distributed file systems (e.g. CORFU)
  Accelerators on FPGAs and GPUs
Storage Optimizations
  High-performance storage devices (e.g. FusionIO)
Network Optimizations
  High-performance network links (e.g. Infiniband)
Chart: Latency of system components (us)
| Flash | FusionIO | 1Gb Ethernet | 10Gb Ethernet | Infiniband
Latency of system components | 100 | 50 | 120 | 50 | 4

## Slide 31: BlueDBM Goals
BlueDBM is a distributed storage architecture with the following goals:
  Low-latency high-bandwidth storage access
  Low-latency hardware acceleration
  Scalability via efficient network protocol & topology
  Multi-accessibility via efficient routing and controller
  Application compatibility via normal storage interface
CPU
RAM
Flash
Network
FPGA
Motherboard

## Slide 32: BlueDBM Node Architecture
Address mapper determines the location of the requested page
  Nodes must agree on mapping
  Currently programmatically defined, to maximize parallelism by striping across nodes

## Slide 33: Prototype System
Topology of prototype is restricted because ML605 has only one SMA port
  Network requires hub nodes

## Slide 34: Controller as a Programmable Accelerator
BlueDBM provides a platform for implementing accelerators on the datapath of storage device
  Adds almost no latency by removing the need for additional data transport
  Compression or filtering accelerators can allow more throughput than hostside link (i.e. PCIe) allows
Example: Word counting in a document
  Controller can be programmed to count words and only return the result
Accelerator
Flash
Host Server
Accelerator
Flash
Host Server
We’re actually building both systems
Notes: Separate in-path to out-path into separate slide ( in prototype results )
Differentiate word counting example from prev slides

## Slide 35: Accelerator Configuration Comparisons
Chart: Bandwidth (MB/s)
| In-datapath | Off-datapath | Software
Bandwidth (MB/s) | 128 | 53 | 31