## Slide 1: Certified Control for Self-Driving Cars
Xin Zhang
joint work with Daniel Jackson, Jonathan DeCastro, Soonho Kong, Dimitrios Koutentakis, Angela Leong Feng Ping, Armando Solar-Lezama, Mike Wang

## Slide 2: self-driving car: a complex system prone to failure
planning
perception
control
sensors
actuators
GPS
reliance on external infrastructure
map
malware with updates
physical device failures
unpredictable ML
software complexity: bugs

## Slide 3: evidence of safety?
Testing?
for 95% confidence in 10-8 failures/mile, need to drive 275M miles
(Kalra et al.)
Notes: https://ts.data61.csiro.au/publications/nictaabstracts/Klein_AEMSKH_14.abstract.pml
Citation

## Slide 4: evidence of safety?
Verification?
SEL4 verification: $400/line 10m lines of critical code: $4B
Notes: https://ts.data61.csiro.au/publications/nictaabstracts/Klein_AEMSKH_14.abstract.pml

## Slide 5: option #1: inline checks
idea
  add inline checks to controller code
  override proposed action if deemed dangerous
example
  Responsibility-Sensitive Safety (Shashua et al)
  ensures safe separation maintained
pros and cons
  + easy to implement
  - may fail to perform check (eg, if compromised)
  - doesn’t protect against flawed interpretation of sensor data
Sensors
Actuators
command
Controller
Checker

## Slide 6: option #2: safety controller
idea
  checks are carried out by independent device
  can veto controller commands even if controller fails
example
  Simplex (Sha et al)
pros and cons
  + checker may be smaller and easier to verify
  + immune to compromise of controller
  - checker requires access to sensors
  - checker must interpret sensor data
major source of failures!
Checker
Sensors
Actuators
command
Controller
command

## Slide 7: option #3: certified control
idea
  like safety controller, but checker has no direct access to sensors
  controller presents certificate to checker, which can be checked without sensors
pros and cons
  + like safety controller, checker is isolated
  + but checker does not require sensor analysis, so easier to verify
  - not clear how to certify all forms of sensor interpretation
Checker
Sensors
Actuators
certificate
Controller
command

## Slide 8: example: certificate for continuing in lane
action proposed by certificate
  continue ahead without decreasing speed
sensor data provided
  a distance D
  3 LIDAR readings L[0..2], signed by LIDAR unit
  current ego car velocity V, signed by velocity unit
what the checker does
D
Notes: Runtime
Instance-based
Design interface
Easy to check

## Slide 9: example: certificate for continuing in lane
Certificate
distance D
LIDAR points with signature
velocity with signature
Checker
LIDAR
points
velocity
D
deceleration
of other car
acceleration
of car
if the lead car suddenly brakes, can our car avoid a collision in the next action cycle?
verified using an SMT solver
Notes: Runtime
Instance-based
Design interface
Easy to check

## Slide 10: a certificate is…
a runtime assurance case
  provides evidence that action is safe
  in terms of physical impact, not just code correctness
  evaluated at runtime, not during development
Notes: Emphasize combination of dynamic and static. Not just property we’re checking, some safety guarantee after check

## Slide 11: a certificate is…
a runtime assurance case
instance-specific
  evidence for this action, not for all actions

## Slide 12: a certificate is…
a runtime assurance case
instance-specific
a designed interface
  agreed in advance by designers of controller and checker

## Slide 13: a certificate is…
a runtime assurance case
instance-specific
a designed interface
easily checked
  exploiting complexity gap between finding a solution and checking one

## Slide 14: a certificate is…
a runtime assurance case
instance-specific
a designed interface
easily checked
unforgeable
  for example, uses signed LIDAR readings
  so controller can’t present spurious sensor data

## Slide 15: status
simulations
  1/10th scale mini racecar with LIDAR JavaScript virtual simulation
assurance case
  arguments for safe separation
  checked with DREAL and Z3

## Slide 16: Simulation using Racecar
Without Certified Control

## Slide 17: Simulation using Racecar
With Certified Control

## Slide 18: Virtual Simulation

## Slide 19: next steps
certificates for other actions
  accelerating, lane switching
map evidence
  including data about position on road in certificate
  also existence of lanes!
  general framework for certificate check
  constraint-based using DReal
other kinds of sensor interpretation
  certification for machine learning more generally
  how would you certify a visual analysis?
Notes: Feedback:
Pathlogical case where the other cars work against you.
SMT solvers are too costly to run at runtime. (Ask Soonhoo, people do us e