## Slide 1: Improving Wireless Network Performance using Sensor Hints
Lenin Ravindranath
Calvin Newport, Hari Balakrishnan, Sam Madden
Massachusetts Institute of Technology
Notes: I will talk about Wireless ESP. Its about using sensors to develop better network protocols. Its joint work with Calvin Newport, Hari and Sam at MIT.

## Slide 2: Big Changes in Access Devices
297M smartphones sold worldwide in 2010
  31% of US phone market; 50% by this year
Smartphones and tablets exceeding PC sales
Notes: Over the past decade, they has been big changes in the usage of internet access devices. We initially moved from desktops to laptops and over the last 2-3 years, there has been a phenomenal increase in the usage of smartphones and tablets.

## Slide 3: Big Changes in Access Devices
Dominant mode of data access in the future

## Slide 4: “Truly Mobile” Devices
Often switch between static and mobile
Exhibit a variety of mobility modes
Move through different environments

## Slide 5: The Problem
Protocols need to adapt to different settings
  Mobility mode impacts wireless performance
Most protocols optimized for static settings
  They perform poorly during mobility

## Slide 6: Static vs. Mobile
Channel constantly changing
  Channel assessments quickly outdated
  Protocols should not maintain long histories
Channel relatively stable
  Protocols can average estimates
  Ignore short-term variations

## Slide 7: Static vs. Mobile
Topology is hardly changing
  Probe for links less frequently
  Compute routes over long time scales
Topology changing rapidly
  Probe for links more often
  Compute routes over shorter time scales

## Slide 8: Current Wireless Protocols
Do not differentiate between mobility modes
Attempt to adapt to different settings implicitly using measurements of packet loss, SNR, BER
… leading to poor performance
Lack of explicit knowledge about prevalent mobility mode

## Slide 9
Proximity
Sensor
Camera
Ambient Light
Sensor
Microphone
Accelerometer
GPS
Compass
Gyro
Notes: And the answer is yes, because with the proliferation of smartphones and tablets, we have an opportunity here.

## Slide 10
Accelerometer
Proximity
Sensor
Camera
Ambient Light
Sensor
Microphone
GPS
Compass
Gyro
Many, many, applications…

## Slide 11
Accelerometer
Proximity
Sensor
Camera
Ambient Light
Sensor
Microphone
GPS
Compass
Gyro
Ignored by Protocols!
Notes: And the answer is yes, because with the proliferation of smartphones and tablets, we have a opportunity here.

## Slide 12
Application
Transport
Network
MAC
PHY
Wireless Radio
Wireless Protocol Stack
Accelerometer
Proximity
Sensor
Camera
Ambient Light
Sensor
Microphone
GPS
Compass
Gyro
Ignored by Protocols!

## Slide 13
Application
Transport
Network
MAC
PHY
Wireless Radio
Wireless Protocol Stack
Accelerometer
GPS
Compass
Gyro

## Slide 14
Application
Transport
Network
MAC
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Hints
Sensor
Info

## Slide 15
Application
Transport
Network
MAC
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Hints
Movement
Direction
Speed
Use hints to adapt to different mobility modes differently
Notes: Add position

## Slide 16
Application
Transport
Network
MAC
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Hints
Movement
Direction
Speed
Use hints to adapt to different mobility modes differently
Mobility hint

## Slide 17
Application
Transport
Network
MAC
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Hints
Movement
Direction
Speed
Use hints to adapt to different mobility modes differently
Hints Protocol
Adapt to hints from neighbors

## Slide 18
Application
Transport
Network
MAC
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Rate Adaptation
Movement
Heading
AP Association
Speed
Vehicular Routing
Walking

## Slide 19
Application
Transport
Network
MAC
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Rate Adaptation
Movement
Heading
AP Association
Speed
Vehicular Routing
Walking
Topo Maintenance

## Slide 20
Application
Transport
Network
MAC
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Rate Adaptation
Movement
Heading
AP Association
Speed
Topo Maintenance
Packet Scheduling
Power Saving
Adapt Cyclic Prefix
Network Monitoring
Speed
Walking
Location
Vehicular Routing

## Slide 21
Application
Transport
Network
MAC
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Rate Adaptation
Movement
Heading
AP Association
Speed
Vehicular Routing
Walking

## Slide 22
GPS
Compass
Accl
Gyro
Movement
Heading
Speed
Walking

## Slide 23
Accl
Movement
Reliably detect movement
within 10-100ms
Is the device
static or moving?

## Slide 24
GPS
Compass
Accl
Gyro
Movement
Heading
Speed
Walking
Walking Hint
  Accelerometer
  Transitgenie (Sensys ‘10)
Heading
  Outdoor - GPS
  Indoor – Compass + Gyro + Accelerometer
Speed
  Outdoor - GPS
  Indoor – Accelerometer?

## Slide 25
Application
Transport
Network
MAC
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Rate Adaptation
Movement
Heading
AP Association
Speed
Walking
Vehicular Routing

## Slide 26
Application
Transport
Network
MAC
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Rate Adaptation
Movement

## Slide 27: Rate Adaptation in Wireless Networks
6 Mbps
9 Mbps
12 Mbps
18 Mbps
24 Mbps
36 Mbps
48 Mbps
54 Mbps
802.11a bit rates
Packet encoded at a particular bit rate
Rate Adaptation:
Finding the best bit rate to transmit a packet

## Slide 28: Static vs. Mobile Performance
Static and walking traces
  Cycle through bit rates
3 different environments
  60 traces
Trace-driven simulation
  TCP throughput
Static | 
Sample Rate | 85 – 99%
RRAA | 80 – 97%
RBAR | 70 – 80%
CHARM | 
Moving | 
Sample Rate | 33 – 59%
RRAA | 45 – 63%
RBAR | 60 – 75%
CHARM | 
Compare to
best post-processed
throughput

## Slide 29: Static vs. Mobile Loss Patterns
Probability that packet i is lost given packet i-k is lost
Losses are more bursty when a node is mobile than when a node is static

## Slide 30: Mutual Information between success/failure events
10 ms
Static vs. Mobile

## Slide 31: Mutual Information between success/failure events
10 ms – 20ms
Different walking speeds

## Slide 32: RapidSample: Rate Selection for Moving Nodes
6 Mbps
9 Mbps
12 Mbps
18 Mbps
24 Mbps
36 Mbps
48 Mbps
54 Mbps
6 Mbps
9 Mbps
12 Mbps
18 Mbps
24 Mbps
36 Mbps
48 Mbps
54 Mbps
6 Mbps
9 Mbps
12 Mbps
18 Mbps
24 Mbps
36 Mbps
48 Mbps
54 Mbps
1. After a single loss
  Reduce rate
2. Short history (10 ms)
  Don’t retry a failed rate
  Or any higher rate
3. Channel not degrading, probably improving
  After few successes, sample higher rate not failed
  If incorrect, come back to the original rate
[failed – within last 10ms]
[failed – within last 10ms]

## Slide 33: RapidSample, when Device is Moving
16% to 75% better throughput than other protocols
Trace-driven (ns3)
30 traces
3 environments
  Office
  Hallway
  Outdoor
TCP throughput

## Slide 34: But when Static…
Up to 28% lower throughput than other schemes
Trace-driven (ns3)
30 traces
3 environments
  Office
  Hallway
  Outdoor
TCP throughput

## Slide 35: Hint-Aware Rate Adaptation
Application
Transport
Network
Rate Adaptation
PHY
Wireless Radio
Wireless Protocol Stack
Accl
Movement
RapidSample when moving
SampleRate when static
Movement

## Slide 36: Implementation and Evaluation
Linux (Click)
Android
Movement hint
SampleRate
RRAA
RapidSample
Hint-Aware
1000 byte packets (at a bit rate)
ACK

## Slide 37: Implementation and Evaluation
2 environments
  Office
  Hallway
10 movement patterns
  Static + Moving
45 – 90 sec long
Average 3 back-to-back trials

## Slide 38: Hint-Aware Rate Adaptation
20%, 17% better than SampleRate on average
22%, 37% better than RRAA on average

## Slide 39: when device is moving
61%, 40% better than SampleRate on average
16%, 39% better than RRAA on average
Hint-aware

## Slide 40: when static…
Hint-aware
24%, 35% better than RRAA on average
43%, 57% better than RapidSample on average

## Slide 41: Critique
Aren’t PHY layer techniques (SoftRate) better?
  Requires PHY changes
  Hint-aware: On traces, ~90% of SoftRate
Isn’t continuous adaptation a better design?
  Cf. mutual information graph
  Hard to measure speed indoors
Is RSSI variation a good indicator for mobility?
  Large variations even when a node is static
  Depends on environment, device, time, RSSI
  Sensitive to movement in environment
Notes: fix

## Slide 42
Application
Transport
Network
MAC
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Rate Adaptation
Movement
Heading
AP Association
Speed
Walking
Vehicular Routing

## Slide 43
Application
Transport
Network
MAC
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Heading
AP Association
Walking

## Slide 44: AP Association: Picking the best AP
Maximize throughput
  File download
Minimize handoffs (scans)
  VOIP – minimize disruptions

## Slide 45: AP Association: Picking the best AP
Scan
Scan
Infrequent scans

## Slide 46: AP Association: Picking the best AP
Static

## Slide 47: Walking-Aware Association
1. Static – Stop Scanning
2. Walking – Scan Periodically
3. Walking to Static – Scan once
Maximize throughput

## Slide 48: Heading-Aware Association
Heading
Minimize Handoff
Training-based approach
  Background Android application
  Training: WiFi scans + Heading hint
  Query the model with current AP and heading hint

## Slide 49: Hint-Aware Association
30% higher median throughput
Android implementation
30 traces; Static + Moving
40% median reduction in handoffs
Throughput
# handoffs

## Slide 50
Application
Transport
Network
MAC
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Rate Adaptation
Movement
Heading
AP Association
Speed
Walking
Vehicular Routing

## Slide 51
Application
Transport
Network
MAC
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Heading
Speed
Vehicular Routing

## Slide 52: Routing in Vehicular Mesh Networks
“V2V”

## Slide 53: Routing in Vehicular Mesh Networks
Longevity of links useful – avoids expensive repairs
Connection Time Estimate (CTE)
  Use heading and speed to predict connection duration
  Link between nodes heading in the similar direction tend to last longer

## Slide 54: Routing in Vehicular Mesh Networks
Longevity of links useful – avoids expensive repairs
Connection Time Estimate (CTE)
  Use heading and speed to predict connection duration
  Link between nodes heading in the similar direction tend to last longer

## Slide 55: Routing in Vehicular Mesh Networks
Longevity of links useful – avoids expensive repairs
Connection Time Estimate (CTE)
  Use heading and speed to predict connection duration
  Link between nodes heading in the similar direction tend to last longer
  Speed is inversely correlated to connection duration
Empirical evaluation on taxi traces
  15 networks, 100 vehicles each
Links with large CTE lasted 4 to 5 times longer
than the median duration over all links

## Slide 56
Application
Transport
Network
MAC
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Rate Adaptation
Movement
Heading
AP Association
Speed
Walking
Vehicular Routing

## Slide 57
Application
Transport
Network
MAC
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Rate Adaptation
Movement
Heading
AP Association
Speed
Topo Maintenance
Packet Scheduling
Power Saving
Adapt Cyclic Prefix
Network Monitoring
Speed
Walking
Location
Vehicular Routing

## Slide 58
Application
Transport
Network
MAC
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Hint Aware Protocols
Movement
Heading
Speed
Speed
Walking
Location

## Slide 59: Hint-Aware Protocol Architecture
GPS
Compass
Accl
Gyro
Sensor Library
Hint Aware Protocols

## Slide 60: Hint-Aware Protocol Architecture
GPS
Compass
Accl
Gyro
UDP
MAC
Sensor Library
Hint Transport Layer
Hint Aware Protocols
UDP Packets
802.11 Frames

## Slide 61: Hint-Aware Protocol Architecture
GPS
Compass
Accl
Gyro
UDP
MAC
Sensor Library
Hint Transport Layer
Hint Aware Protocols
Sensor
Hint Manager
REGISTER
SEND
Query
Hints
Hints
Hint Service
UDP Packets
802.11 Frames
Hints
Received Hints
- Android Service
- Linux Click Module

## Slide 62: Limitations
Energy
  Accelerometer, Compass is cheap but GPS is not.
  Dynamically adapt sample rates
  Triggered sensing
  Low cost sensing - training based
Calibration across device types
  Movement hint required no calibration
  Walking hint required tuning
Privacy

## Slide 63: Related Work
Wireless power saving
  WakeOnWireless: Low power radio
  Cell2Notify: GSM radio to wakeup WiFi
  Blue-Fi: Bluetooth and GSM to predict WiFi
AP selection
  Mobisteer: Location and speed to select AP and antenna orientation
  Breadcrumbs: Use location to build a HMM
Rate Adaptation
  CARS: Train using speed and heading from GPS

## Slide 64: Take-Away Message
Truly mobile devices will soon be dominant
  Variety of mobility modes poses problems for wireless protocols
Sensors on these devices give us a new opportunity to develop network protocols
Protocol architecture using sensor hints can significantly improve MAC, link, network layers

## Slide 65: Backup

## Slide 66: Probing
How frequently should nodes probe?
Delivery Probability
ETX, ETT
Probes

## Slide 67: Infrequent Probing
Inaccurate link estimation leads to
poor throughput

## Slide 68: Frequent Probing
Probing wastes bandwidth

## Slide 69: Delivery Probability
Mobility causes delivery probability to
fluctuate with bigger jumps

## Slide 70: Static vs. Mobile
Mobile case requires 20x more probes
to maintain acceptable estimation error

## Slide 71: Adaptive Probing Protocol
Adapt probing based on movement hints
When a node is static
  Probe infrequently (1 probe every 2 seconds)
When a node is mobile
  Probe frequently (10 probes per second)

## Slide 72: Adaptive Probing
Tracks the link accurately with fewer probes

## Slide 73: Pruning association

## Slide 74: AP Association
Scan
Scan
Scan
Infrequent scans

## Slide 75: Static vs. Mobile Loss Patterns
Losses are more bursty when a node is mobile than when a node is static
Probability that packet i+k is lost given packet i is lost

## Slide 76: Static vs. Mobile Loss Patterns
Probability that packet i+k is lost given packet i is lost
10 ms
Losses are more bursty when a node is mobile than when a node is static
k

## Slide 77: RapidSample vs. SoftRate
Comparable throughput to Softrate
Sigcomm 2009
10 traces
Moving
TCP throughput

## Slide 78
Application
Transport
AP Association
MAC
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Heading
Walking
Improve throughput
Reduce
handoffs
Notes: Get rid of this

## Slide 79: Hint-Aware Rate Adaptation
Trace driven (ns3)
30 traces
3 environments
Static + Moving
TCP throughput
52%, 30%, 22% better than SampleRate on average
27%, 17%, 39% better than RRAA on average
47%, 11%, 27% better than RBAR on average
Notes: Delete this

## Slide 80: Hint-Aware Rate Adaptation
Application
Transport
Network
Rate Adaptation
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Movement
Movement
Improve throughput
Notes: Get rid

## Slide 81
Application
Transport
V Routing
MAC
PHY
Wireless Radio
Wireless Protocol Stack
GPS
Compass
Accl
Gyro
Heading
Speed
Predict link duration and quality
Better routing

## Slide 82: Hint-Aware Protocol Throughput

## Slide 83: Hint-Aware Protocol Throughput