## Slide 1: DogBOT
Team 6 –
Kuan-Ting Yu
Wei How Mo
Ping-Che Shiao
Issue Lee

## Slide 2: Outline
Gesture recognition - Kinect
Human following - laser range finder
Chase ball - color camera
Facial expression - emotion

## Slide 3: Gesture
Stereo Vision
  Compare two images to extract 3D info.
  But, depth image become broken for area with less texture
Alternative: Kinect Sensor

## Slide 4: Kinect
Kinect is an active sensor which projects structured infrared light on objects.
  use the dot pattern to derive 3D information
  with built-in body parts tracker
http://boingboing.net/2010/11/23/dancing-with-invisib.html
Notes: depth image is much more complete
interprets 3D scene information from a continuously-projected infrared structured light

## Slide 5: Stereo v.s. Kinect

## Slide 6: Gesture Recognition
We have designed the finite state machine to recognize the 5 gestures for interaction.
But, later we utilize Kinect’s built-in gesture recognizer.
Gestures | State 1 | State 2 | State 3 | State 4 | Complete
HELLO |  |  |  |  | 
INTRODUCTION |  |  |  |  | 
COME |  |  |  |  | 
CHASE |  |  |  |  | 
STOP |  |  |  |  | 

## Slide 7: Human Following
Laser Scanner
  High precision and scan rate
  Invariant to different lighting conditions, perspective change, etc
Flow Chart:
Human legs detection
robot navigation
Filtering
(with cues from Kinect)
(not yet ready)
(done)
Notes:   Our human following is based on laser scanner, because laser has high precision and scan rate, and it is Invariant to different lighting conditions or perspective change,
  This is the flow chart of our human following system
  first we detect the human legs, and we want to fuse laser with Kinect to locate human more precisely, and in the next step we move the dogbot.

## Slide 8: Human Following
Human detection using laser scanner
  Detection position : lower legs
Sensing Field
Lower leg
Notes: In our human legs detecting, we detect human lower legs, and list all the possible of human leg's pattern to classify it as a human.

## Slide 9: Human Following
Obstacle Avoiding:
  Laser based
  Front of pioneer, degree 45 to degree 135
Notes:   And next is the obstacle Avoiding: it’s laser based, our detecting region is front of pioneer about 60cm, degree 45 to degree 135,

## Slide 10: Ball chasing
calculate hue histogram of the ball
back projection on current image
thresholding and finding contour
coordinate transform from image to base

## Slide 11: Coordinate transform
To achieve higher level planning, precise target localization is a plus.
x
y
z
x
y
z
Notes: { }^{base} p = { }^{base}T_{cam}{ }^{cam}T_{img}{ }^{img}{p}

## Slide 12: Recall
Depth is not fixed in our case!

## Slide 13: Our solution (1/2)
x
y
z
x
y
z
is measured by hand.
is measured by calibration tool as extrinsic parameter.
x
y
z
Notes: { }^{base} p = { }^{base}T_{cam}{ }^{cam}T_{img}{ }^{img}{p}

## Slide 14: Our solution (2/2)
x
y
z
x
y
z
x
y
z
, the inverse perspective transform, can be solved by extending the constraint of fixed depth, , to a general plane equation of the ground:
Notes: (\mathbf{p}-\mathbf{o}_{board})\cdot \overrightarrow{n}=0

## Slide 15: Experimental result
The system can locate ball within 5m from camera with precision around 10cm.

## Slide 16: Summery
Gesture recognition - Kinect
Human following - laser range finder
Chase ball - color camera
Facial expression - emotion