## Slide 1
Image Enhancement Using Calibrated Lens Simulations
Yichang Shih¹, Brian Guenter², Neel Joshi²
MIT CSAIL¹, Microsoft Research²
Goal: Remove optical aberrations
Our Method
Challenge
Calibration (Optimization)
Applications
Results
Acknowledgement
All lenses have optical aberrations [Seidel, 1856]
Spherical aberration
Chromatic aberration
The aberrations can be restored by deconvolution, but requires accurate lens point spread functions (PSFs) info
PSFs are spatially-variant, and changing with focal distance. Measuring all PSFs is expensive
We compute PSFs using the lens CAD model, called lens prescription, by geometric-wave hybrid ray tracing
The model includes - Number of glasses - Dispersion function - Radius, xyz positions of each glass - Dispersion coefficients (C1…C6)
n:refraction index)
n2 - 1 = C1λ2/(λ2-C2) + C3λ2/(λ2-C4) +… C5λ2/(λ2-C6)
Image enhancement on cloud - The server keeps an lens prescription for each lens
Remove chromatic aberrations, distortions, and sharpen the image
We target at mobile phone cameras - Small lenses (diameter 6~18mm) - Prime lenses
Pinhole arrays (light sources) 20x20 holes
Camera
Lens
PSFs measurement
The simulation is different from the measurement
The lens manufacturing tolerance can cause the actual lens prescription different from the spec
Our solution: taking the spec and measured PSFs at a single distance as input, calibrate the accurate lens prescription for image enhancement
We can predict PSFs at any positions and focal distances
We use a monochromatic camera and exposure under r/g/b different lighting instead of demosaicing
Objective function: L2 norm between measured & synthetic PSFs
Optimization: gradient descent
Variables: parameters in lens prescription
Initial parameters: provided lens prescription from the manufacturer
Fitted | measured | unfitted
unfitted | fitted
Fitting using measurement at 279 mm, and synthesize PSFs at 368 mm
Fitted
Measure
Unfitted
Every lens needs to be calibrated once
We would like to thank Edmund Optics for providing the lens prescriptions. Thank Fredo Durand for helpful discussion
PSF
PSF
279mm
279mm
368mm
Deconvolution result