## Slide 1: Compass: Navigating the Design Space of Taint Schemes for RTL Security Verification
Yuheng Yang* (MIT), Qinhan Tan* (Princeton)
Thomas Bourgeat (EPFL), Sharad Malik (Princeton), Mengjia Yan (MIT)
*Co-first Authors
Notes: Hello everyone, I am Yuheng Yang from MIT. I am going to present Compass, navigating the design space of taint schemes for RTL security verification. It’s a collaborated work with Qinhan, Thomas, Sharad, and my advisor Mengjia.

## Slide 2: Hardware Security Problems
Side channel attacks
Spectre attacks
TEEs root-of-trust key leakage
……
Violations of
Information Flow Property
Notes: Nowadays, we are facing many hardware security problems, such as side channel attacks, Spectre attacks, TEE root-of-trust key leakage, etc. In our opinion, they are all fundamentally some violations of the information flow property.

## Slide 3: Information Flow Property
secret
Gates /
Registers
Information flow property checks whether a secret can influence the value of attacker observable signals
Notes: More generally, information flow property checks whether some secret can influence the value of attacker observable signals. In the context of hardware security, given a secret located in a victim’s domain, the property checks all potential leakage paths from the secret, going through many gates and registers in the hardware, and eventually reach a signal that is observable to attackers. To verify such properties, the community has a widely used technique called taint analysis.

## Slide 4: Taint Analysis
1
Taint Bits
Taint Propagation Logic
?
Output Taint
secret
Gates /
Registers
public
0
Taint analysis over-approximates information flow
Notes: So, what is taint analysis? It uses taint bits to represent whether a signal in the original design might contain secret or not. For example, we assign taint bit 1 to secret inputs and assign taint bit 0 to public inputs. Then, this taint bit will propagate through the hardware via a concept called taint propagation logic, which essentially computes the value of taint bits for all signals in the design. And eventually, we want to know the value of taint bit associated with this output signal. If it has a value of 1, it means there is likely some leakage. And if it is 0, means there is no leakage. In summary, taint analysis manages to over-approximate information flow by using those taint bits and taint propagation logic.

## Slide 5: Overview
low-overhead
low-precision
high-overhead
high-precision
Different Taint Schemes
Simple & Precise
Automated Algorithm
Observation: There is a large design space of taint schemes
Goal: Find taint schemes that are simple and precise
Solution: An automated, iterative approach to find efficient taint schemes
Technique:
Counterexample-guided Taint Refinement
Notes: In our project, we start from one key observation of taint analysis, which is, there actually exist a large design space of taint schemes. This space can be visualized using a spectrum where taint schemes on the left have low overhead and low precision, and schemes on the right have high overhead and high precision. The goal of our project is to find a design point in the middle, which can balance the overhead and precision by being both simple and precise. To find this design point, we develop an automated and iterative approach. At the core, we use a technique called counterexample-guided taint refinement. To get you started on understanding our work, I will first introduce this large design space of taint schemes.

## Slide 6: Design Taint Schemes
Overhead (# gates)
Precision
Naïve
Precise*
A
B
O
AND Gate
❌ False Leakage
❌ ~4x Overhead
 Slow Verification
A_taint
B_taint
O_taint
Naïve Taint Logic
Naïve taint logic introduces false flow
A | B | O | Leakage ? | O_taint
0 | 0 | 0 | No | 1
1 | 0 | 0 |  | 
*Complete Information Flow Tracking from the Gates Up. Mohit Tiwari, et al. 2009.
Notes: Firstly, consider a single AND gate which takes in inputs A, B and generates output O. There are various ways to design taint logic for it, which can be summarized using this 2-dementional space. In the x-axis, we care about the overhead of taint logic, quantified using number of gates used in taint logic, and y-axis represents the precision achieved from taint logic, which I will explain more with examples.
The simplest version of taint logic is called naïve taint logic, which will take in the taint bit of all input signals, and use an OR gate to compute the output taint bit. It essentially states, if any one of inputs is tainted, then the output will be tainted. This taint logic has the benefit of being simple, using a single gate to propagate taint. But it has the problem of giving false leakage, resulting it being very low on the precision metric.
I am going to use this truth table to help you understand why it introduces false leakage. Suppose input A is secret and B is public. The two rows in the table compare 2 cases where A is taking different values and B is always 0. In both cases, the AND gate outputs 0, which essentially means no matter how you change the secret value, it cannot affect the output, and thus there is no leakage to the output. However, our naïve taint logic does not realize this special behavior and mistakenly taints the output, introducing a false leakage.
To avoid such false leakage, more precise taint logic is proposed. However, it comes with a cost. We find that for a standard processor, it can introduce as much as 4 times the overhead. If you directly use it to verify security, it will be very slow. Now that we understand this trade-off between naïve and precise taint logic for a single AND gate, let’s move on to taint logic for a whole circuit …

## Slide 7: Design Taint Schemes
Always Use
Naïve Taint Logic
Always Use
Precise Taint Logic
Ours
Mixing Taint Schemes
❌ Slow Verification
❌ False Leakage
Naïve
Taint Logic
Precise
Taint Logic
Overhead (# gates)
Precision
Notes: … composed of many gates. Similarly, one design choice is always using naïve taint logic for all gates, and it will suffer from false leakage. We can also change to always use precision taint logic, and suffer from slow verification. However, because now we are considering so many gates, we actually have lots of other options of mixing naïve and precise taint schemes. It means that for some gates, we use naïve taint logic to save the budget, and for other gates, that are potentially more important to secret propagation, we use precise taint logic. These mixing choices are basically what we want to explore in our project. Then, the question is that how would this mixture look like. Will we be able to use naïve taint logic at lots of places to significantly reduce the overhead?

## Slide 8: Advantage of Mixing Taint Schemes
Design:
Property:
  Prove that if inst_type==ADD, then commit_taint==0
Single-Cycle Adder
Zero-Skip Multiplier
secret
mul_finish
add_finish
commit
inst_type
Challenge: How to automatically discover gates that need precise taint logic?
result
result
= ADD
Precise
Taint Logic
Naïve
Taint Logic
Notes: To show you the advantage of mixing taint schemes, I will use a concrete example. It's a design consisting of a single-cycle adder, and a multiplier with the zero-skip optimization, meaning it takes a fast path if inputs contain zero, and takes a slow path otherwise. We will feed some secret value into both modules, and they will produce results that are affected by secret. However, when you consider the finish signals for these two modules, the adder, as a constant-time module, it produces a public finish signal, but the multiplier, due to the zero-skip optimization, produce a secret one. Finally, there will be a mux gate to select between two finish signals based on the instruction type and produce the commit signal that we consider to be observable by attackers.
Given this design, we want to analyze a security property that proves, if the instruction type is ADD, then the commit signal should not be tainted. The reason that this property holds is very simple: Because we are executing add, the mux will select add_finish as the commit signal, which does not contain secret. In order for taint logic to correctly analyze this scheme, we need to have precise taint logic for this mux, because, if you just use naïve taint logic, it will say hey, there is one input to the mux called multiplier done being tainted, so naïve taint logic will taint the output commit signal. But precise taint logic will not make this mistake. Regarding the taint logic for other modules, for the multiplier, we can just use naïve taint logic, because we know the output will be tainted anyway. And for the adder, we can mostly use naïve taint logic, but just be a little careful with add_finish signal and make sure is it not falsely tainted.
So, with our manual analysis, we get this ideal mixture of taint logic with very little overhead, where only a few gates need precise taint logic. However, this design process is kind of manual and utilizes a lot of high-level understanding about the design. The challenging part of our project is, how to automatically discover those gates that need precise taint logic. The solution we provide is called …

## Slide 9: Compass Framework
Key Procedure
naïve taint scheme
precise taint scheme
Simple & Precise
Model
Checker
Automated Algorithm
Different Taint Schemes
Automated Counterexample-Guided Taint Refinement
False
Counterexample
Security Proof /
Valid Attack
Notes: … Compass, which is an automated counterexample-guided taint refinement framework. Given this spectrum of different taint schemes, and the goal of finding this mixture of taint schemes that is both simple and precise, our solution starts from the simplest design point and try to use it to verify security with a model checker. The model checker will give us a false counterexample or a false leakage. We call it false because it comes from the imprecision of our naïve taint logic, it does not come from a real security bug of our design.
We then use this false counterexample to improve our taint logic. Specifically, we design an automated algorithm to analyze the counterexample and locate specific gates that require precise taint logic. Then we refine the taint logic for these gates, and we do the counterexample-guided refinement again and again, and eventually, find an ideal taint logic that either gives a formal security proof, or discover a valid attack. One note is that if Compass gives a security proof at the end, even using lots of naïve taint logic, it is still a valid proof because naïve taint logic does not miss any secret flow, it only over-approximates flow. So, given this overview, the next part of my talk will go a little deeper into the automated algorithm for refining taint schemes, which is the key procedure in our refinement loop.

## Slide 10: Refinement Problem Setup
1
2
3
4
5
6
sink
Tainted Flow
source
View circuit as a graph
Color edges based on taint propagation results
View taint refinement of a gate as a “cut” on graph
Public Flow
Falsely Tainted Flow
Taint Refinement
Eliminate false counterexample = Find cuts on graph
Notes: I will start by giving you a little more setup about this problem, to let you understand the refinement problem better. Firstly, we view a circuit design as a graph. The nodes represent gates in the design and edges represent connections among gates. The graph has a secret source signal and a target sink signal that we do not want secret flow to.
Secondly, we color the edges based on the taint propagation results, where we will use black arrows to represent public flows and red arrows to represent tainted flows. For example, if we analyze this design with naïve taint logic, it will mark most of the flow as red, because naïve taint logic basically taint all signals that are connected to the source. Furthermore, we can also identify part of the tainted flow as falsely tainted flow and marked it using dashed lines. These dashed lines essentially mean, if we have the most precise taint scheme, these dashed taint propagation flow shouldn’t exist. And in the paper, we have an algorithm to find these false flow.
With this concept of false flow, we now can view the taint refinement of a gate as a “cut” on the graph that tries to remove those falsely tainted flows. Specifically, we use a scissors icon to represent a taint refinement, and if a refinement is an effective cut, I will just remove the false flow it produces. So now, our problem of eliminating false counterexample is essentially finding sufficient cuts on this taint propagation graph, to remove the false flow at the sink signal. Before I present our solution to graph cut problem, …

## Slide 11: Some Complications…
1
2
3
4
5
6
sink
source
Not all refinements can effectively remove false flows
Given a false flow, there can exist multiple effective cuts to remove it. Which one works better?
Sometimes, we need to make multiple cuts together to remove a false taint
Tainted Flow
Public Flow
Falsely Tainted Flow
Taint Refinement
Notes: I want to describe some complications of it, to give you some taste of the challenge we are facing. First, not all refinements can effectively remove false flows. The reason is that, for some gates, it already takes in lots of false tainted signals, and no matter how improve the taint logic for this gate, it does not help. Second, given a false flow, there can exist multiple effective cuts to remove it. Then the question is, which one works better? For example, for the flow 3 to 4 and to 6, we can have multiple cuts, represented using these 3 scissors, but should we cut on gate 3 or gate 6? This is also one thing we need to consider. And lastly, sometimes, we need to make multiple cuts together to remove a false taint. For example, both flow 4 to 6 and flow 5 to 6 contribute to the sink, then the challenge would be how to discover and cut all of them? We have more detailed analysis of these complications in the paper, but in this talk, I will just jump to our solution, …

## Slide 12: Our Iterative Algorithm
current
1
2
3
4
5
6
sink
source
Tainted Flow
Public Flow
Falsely Tainted Flow
Taint Refinement
Counterexample
Eliminated?
No
Next Counterexample
Yes
Refine “earliest” gate that introduces false flow
False Counterexample
Notes: … which an iterative algorithm to refine the taint logic. It starts with a false counterexample, and it will refine the earliest gate that introduce false flow. It then checks whether the counterexample can be eliminated. If it is not, we go back and make a next refinement, until eventually, we manage to eliminate this counterexample and move on to the next one.
I will also give you a test run of this algorithm on our toy example on the right. The first step is to find the earliest gate that introduce false flow, which is achieved through a backtracing algorithm. The algorithm will start at the sink and try to find all input signals that are falsely tainted. In our example, there are two of them. Then, it will select an arbitrary one to trace back, and again, find inputs that are falsely tainted. It then trace back to gate 3 and because it has no falsely tainted inputs, we do not trace back anymore and will apply a refinement on this gate. With this refinement, we can see part of the false flow is removed, but it still not fully removes the false flow to the sink signal. So, we need to run another iteration of refinement. Now the earliest gate become gate 5 and after refine it, we can eliminate the false counterexample.
This essentially concludes our refinement algorithm on this toy example. One last thing I want to talk about before evaluation is that, how will this refinement look like on realistic hardware?

## Slide 13: Analysis of Refinement Results
Single-Cycle Adder
Zero-Skip Multiplier
secret
mul_finish
add_finish
commit
inst_type
= ADD
Precise
Taint Logic
Recall our toy example:
It is common in Rocket, e.g.,
mem_data
alu_data
csr_data
inst_type
wb_data
Finding: Most taint refinements target gates that operate at the boundary
between secret & public signals
Notes: In this slide, I will give you a brief analysis of the refinement results. Recall that, we used to have this toy example early-on, which includes a single cycle adder and a zero-skip multiplier. We found that the mux that select between add finish and multiply finish is actually very important to ensure security and requires precise taint logic. Because, it takes in both public and secret data. We find this type of precise taint logic is very common in our case study. For example, in Rocket, we have a similar mux to select among several data sources to produce the writeback data. And because one of the input data, the memory data can be tainted, we need to use a precise taint logic for the mux. In summary, we have the finding that most of these taint refinements target gates that operate at the boundary between secret and public signals, which matches our high-level understanding of the design. Finally, let me show you some evaluation results.

## Slide 14: Result 1: Lower Taint Overhead
Original Design
Added Taint Logic
84% fewer taint gates
Security Property: Secure speculation1
Baseline: CellIFT2
1Hardware-Software Contracts for Secure Speculation. Marco Guarnieri, et al. 2021.
2CellIFT: Leveraging Cells for Scalable and Precise Dynamic Information Flow Tracking in RTL. Flavien Solt, et al. 2022.
Notes: The first result shows that Compass achieves lower taint overhead. This figure shows that, across four processors, how many logic gates are needed for a baseline scheme called CellIFT, which generates the most precise taint logic for the whole design. Data is normalized to the gates in the original design. For example, in sodor, the left bar shows the size of original design. And in the right bar, the first part is just duplicating the original design, and the rest is the added taint logic to analyze information flow. On average, it needs a ratio of 3.93 original gates for the baseline scheme. With compass, we can reduce this ratio to only 1.46. This essentially means Compass achieves 84 percent fewer taint gates. This reduction all come from our mixing naïve and precise taint schemes in the whole design.

## Slide 15: Result 2: Faster Simulation
Benchmarks: median, rsort, qsort, matrix_mul, rsa
32% less simulation time
Notes: Next, we test this taint logic in a common scenario where we simulate the taint logic to analyze information flow. This figure shows that the baseline scheme introduces an overhead of 4.51 times. But after we find a simpler taint scheme with Compass, we can reduce this overhead to a ratio of 3.05, representing a 32 percent reduction on simulation time.

## Slide 16: Result 3: Faster Model Checking
 | CellIFT | Compass | 
 | Proof Time | Proof Time | Time to Find Taint Scheme
Sodor | 2 h | 10 s | 5 min
 | CellIFT | Compass | 
 | Bound with 7 days | Bound with 24 h | Time to Find Taint Scheme
Rocket | 41 | 159 | 1 h
BOOM | 26 | 28 | 31 h
ProSpeCT | 29 | 29 | 35 h
Faster Proof
Check More Cycles
Unbounded Proof
Bounded Proof
Notes: Finally, we also use the taint scheme to do model checking and show Compass is also faster. There can be two types of results of model checkers, unbounded proof or bounded proof. For simple processor like sodor, the baseline scheme gives an unbounded proof with 2 hours. And our scheme, Compass, can give the proof in just 10 seconds. Additionally, we show the time Compass takes to find the taint scheme, which is basically the time to run the refinement loop, including generating all those false counterexamples. And it takes 5 minutes. The results show Compass can achieve faster proof.
For more complex processors, we can only achieve bounded proof. If you check the first row corresponding to Rocket, baseline can only do a bounded proof for 41 cycles in 7days, versus our scheme can check up to 159 cycles in just 24 hours plus 1 hour refinement time. It shows Compass can check more cycles in the bounded proof case.

## Slide 17: Conclusion
Compass finds simple yet precise taint schemes,
enabling faster security verification
https://github.com/MATCHA-MIT/Compass
naïve taint scheme
precise taint scheme
Simple & Precise
Model
Checker
Automated Algorithm
False
Counterexample
Compass:
Notes: In conclusion, we present the Compass framework, and shows it can find simple yet precise taint schemes, enabling faster security verification. The framework is open-sourced on github. That’s all and I am happy to take any questions.