## Slide 1: Lightning: a Reconfigurable Photonic-Electronic SmartNIC for Fast and Energy-Efficient Inference
Zhizhen Zhong
MIT CSAIL
Mingran Yang Jay Lang Christian Williams Liam Kronman Alexander Sludds
Homa Esfahanizadeh Dirk Englund Manya Ghobadi
Notes: Good afternoon everyone. I am Zhizhen Zhong from MIT.
Today I am going to talk about our work, Lightning, a reconfigurable photonic-electronic smartNIC for fast and energy-efficient inference.

## Slide 2: The machine learning (ML) storm
[1]: fastest growing online application ever
[1] https://www.theguardian.com/technology/2023/feb/02/chatgpt-100-million-users-open-ai-fastest-growing-app
In just one month, ChatGPT served 100 million unique visitors.
(Instagram took 2 years)
ML inference empowers a wide-range of applications.
As a result, billions of ML inference packets are flooding data centers.
Massive implications for rethinking our networks and systems.

## Slide 3: Requirements for serving real-time inference packets
[2] https://learn.microsoft.com/en-us/azure/cloud-adoption-framework/innovate/best-practices/ml-deployment-inference
[3] https://towardsdatascience.com/chatgpts-electricity-consumption-7873483feac4
Latency:
  Live inference query response time should be less than 100 ms[2].
Energy consumption:
  ChatGPT’s monthly electricity consumption is more than a 175,000 people[3].

## Slide 4
The first smartNIC system to serve real-time inference packets using photonic computing.
This talk: Lightning

## Slide 5: What is photonic computing?
Use light waves to perform computation in the analog domain.
Computers were born analog.
Charles Babbage conceptualized computers in 1840s as analog devices.
Optical neural network accelerator
Psaltis et al., Opt. Lett. 1985[3]
[3] Demetri Psaltis, and Nabil Farhat. "Optical information processing based on an associative-memory model of neural nets with thresholding and feedback." Optics Letters 10, no. 2 (1985): 98-100.

## Slide 6: Photonics can revolutionize computing
Computes at 100 GHz.
  Tens of times faster than electronics.
Consumes 40 atto Joules (10-18) per multiply-accumulate operation[4].
  Hundreds of times more energy efficient than electronics.
  But photonic computing has never gained practical traction!
[4] Alexander Sludds, Saumil Bandyopadhyay, Zaijun Chen, Zhizhen Zhong, et al.
"Delocalized photonic deep learning on the internet’s edge." Science 378, no. 6617 (2022): 270-276.
Silicon photonic computing chip at MIT[4]

## Slide 7: Photonic computing: modulating light intensities as it propagates
Optical
Modulator
Carrier light
Modulated light
(electrical data)
0.8
0.6
0.7
0.1
0.8
0.6
0.7
0.1
1
1
1
1
Laser
Voltage
0.48
0.51
0.035
0.1
Optical
Modulator2
(electrical data)
0.6
0.85
0.05
1
Voltage
Photo-
detector
(electrical result)
0.48
0.51
0.035
0.1
Double-modulated light
Voltage
Optical modulators and photodetectors are passive devices, which perform the computation naturally as light propagates through the system.
(electrical result)

## Slide 8: Challenge: photonic operations are mixed with electronic ones in real-world ML inference
ReLU
Flatten
Multiply
Accumulate
ReLU
Mul.
Softmax
6
Acc.
Mul.
Acc.
Pkt processing
Pkt processing
Photonic domain
Photonic domain
Photonic domain
A control logic is needed to coordinate the operations across electronics and photonics.

## Slide 9: Even harder challenge: reconfigure photonic-electronic operations for different ML inference
Diverse ML inference packets require a runtime reconfigurable system:
  ML models have relatively small number of computing “templates”: fully-connected layers, convolutions, ReLU, etc.
  Diverse number of combinations of “templates”: e.g., 30 convolution layers.
How to achieve reconfigurable control from packets to photonics?
Pkt processing
Photonic
multiply-accumulate
Digital compute
Photonic
multiply-accumulate
Digital compute
Photonic
multiply-accumulate
Digital compute
… 30 layers…
Photonic
multiply
model #1
model #2

## Slide 10: Strawman approach: Stop-and-go data movement between digital & photonics
ReLU
Flatten
Photonic
multiply-accumulate
Digital accumulate
ReLU
Photonic
MAC
Softmax
Acc.
Photonic
MAC
Acc.
Packet processing
To achieve reconfigurability, the control plane logic is deeply coupled with the data plane operations.
Slows down the critical data plane latency, increases energy consumption
Slow!
Control plane logic
Data plane pipelined operations
How to achieve reconfigurability at runtime without compromising latency?

## Slide 11: Our solution: co-design photonics and digital systems
Control plane logic
ReLU
Flatten
Photonic multiply-accumulate
Digital Accumulate
ReLU
Ph. MAC
Softmax
Acc.
Ph. MAC
Acc.
Packet processing
Abstraction
Abstraction
Abstraction
Abstraction
Abstraction
Abstraction
Abstraction
Abstraction
Abstraction
Abstraction
Key innovation: a hardware programming abstraction to make control decisions on the data plane.
Design goal: simple, yet effective and powerful to cover a wide range of DNNs.

## Slide 12: Lightning’s reconfigurable count-action abstraction
Action
result < target
result == target
Count
module datapath_module {
counts: {
// variables to be counted
}
targets: {
// a set of target results
}
actions: {
// actions to be triggered
// when the result is
// equivalent to the target
}
};
variable
High-level idea: Trigger an action whenever the count result reaches the target.

## Slide 13: Putting it all together: Lightning SmartNIC
100 Gbps Ethernet
PCIe
Packet
1
3
5
6
7
Packet Parser
Synchronized Data Streamer
Photonic
computing
cores
Preamble Detection
Pipeline Parallel Digital Computation
Result Generation
DAG
Configuration
Loader
2
4
DACs
ADCs

## Slide 14
100 Gbps
Ethernet interface
Lightning datapath on FPGA
ADC ports
DAC ports
Photodetector
Modulator
Modulator
Modulator
Modulator
Laser input wavelength #1
Laser input wavelength #2
Lightning prototype at MIT
Notes: We spent about past two years building the first fully-functional Lightning smartnic hardware prototype in our optics lab at MIT. Our hardware prototype contains an 100 Gbps ethernet interface, and a lightning datapath implemented on FPGA with RF DACs and ADCs. In the photonics side, we have four modulators and one photodetector capable of running two multiply-accumulate operations in parallel at 4 GHz.

## Slide 16
100 Gbps
Ethernet interface
Lightning datapath on FPGA
ADC ports
DAC ports
Photodetector
Modulator
Modulator
Modulator
Modulator
Laser input wavelength #1
Laser input wavelength #2
Lightning prototype at MIT
Notes: We realize building such a experimental setup presents a high bar of entry for the SIGCOMM community. So we consolidate our setup and presents an open-source developer kit.

## Slide 17: Lightning open-source developer kit
If you’re interested, please sign up for a kit at https://lightning.mit.edu.

## Slide 18: Large-scale simulations: latency and energy gains
Chart: 
| AlexNet | ResNet-18 | VGG-16 | VGG-19 | BERT | GPT-2 | DLRM
A100 GPU | 787.716 | 276.5137 | 326.4704 | 219.2696 | 60.5109 | 23.6905 | 664.7843
A100X DPU | 776.2408 | 277.1499 | 324.3403 | 214.7331 | 61.0895 | 23.618 | 631.1879
Brainwave | 55.4977 | 37.8663 | 41.466 | 33.0666 | 23.1393 | 13.5029 | 94.701
Inference Latency Speedup
Chart: 
| AlexNet | ResNet-18 | VGG-16 | VGG-19 | BERT | GPT-2 | DLRM
A100 GPU | 623.4518 | 472.5715 | 484.3162 | 337.7201 | 242.0053 | 101.9455 | 205.0002
A100X DPU | 739.0076 | 564.554 | 583.3576 | 404.1923 | 287.4794 | 121.3392 | 235.3385
Brainwave | 71.1753 | 42.9337 | 48.2596 | 39.0131 | 26.3698 | 14.9509 | 140.0977
Energy Savings
Lightning improves the average inference serve time by 42× - 337× while reducing the energy consumption by 54× - 419×.

## Slide 19: Concluding summary
Lightning is the first photonic-electronic smartNIC to serve real-time inference packets.
Open-source hardware and software available at https://lightning.mit.edu.
Our count-action abstraction enables runtime control and reconfiguration of photonic-electronic computation tasks without interrupting the dataflow.
Action
result < target
result == target
Count
variable

## Slide 20: More resources
SIGCOMM 2023 full paper: https://people.csail.mit.edu/zhizhenzhong/papers/2023_SIGCOMM_Lightning.pdf
SIGCOMM 2023 Demo abstract: https://people.csail.mit.edu/zhizhenzhong/papers/2023_SIGCOMM_Lightning_Demo.pdf
SIGCOMM 2023 talk recordings: https://youtu.be/h169d_0JZWE?si=TO-MfFu0b0TByKDH&t=55